## Slide 1: A Memory Benchmarking Characterisation of ARM-Based Systems-on-Chip
Thomas Wrigley
University of the Witwatersrand, Johannesburg, South Africa
GRID 2014, Dubna

## Slide 2: Overview
Introduction
Using SoCs for DSC
Benchmark Results
Discussion & Analysis
Future Work & Next Steps

## Slide 3: Data Stream Computing
High throughput
No/limited offline storage
Programming simplicity
Requires real-time processing of large amounts of data – must address bandwidth efficiency and memory latency issues

## Slide 4: Key Challenges
Some of the problems and concerns faced:
Energy-efficiency
Offline storage capacity
Cost (hardware, electricity, cooling)
Memory latencies & bandwidth inefficiencies

## Slide 5: Existing/Previous Work
Relevance of memory performance being increasingly more widely acknowledged
Lots of military-led and/or -funded research (DIS & HPCC)
Graph500 Benchmark & Green Graph500 (2010 – present)
High Performance Conjugate Gradient (HPCG) benchmark – proposed successor to High Performance LINPACK (HPL)  Jack Dongarra
Intel has proposed using COTS i7s for signal processing

## Slide 6: Using SoCs for DSC
Looking at the potential for use of SoCs
Low Power
Low-Energy Consumption
Require many SoCs – potential for large parallelism
Potentially more energy-efficient
Commercial off-the-shelf (COTS) components
Implementation & usage tends to be easier

## Slide 7: Using SoCs for DSC (continued)
Tested three ARM-based SoCs
Consumer-grade ARM chips tend not to have ECC RAM
Potentially problematic
Will test in due course

## Slide 8: General Specifications
 | Cortex-A7 | Cortex-A9 | Cortex-A15
Cores | 2 | 4 | 4 (+ 4 Cortex-A7)
Max CPU Clock (MHz) | 1008 | 996 | 1596

## Slide 9: General Specifications
 | Cortex-A7 | Cortex-A9 | Cortex-A15
Cores | 2 | 4 | 4 (+ 4 Cortex-A7)
Max CPU Clock (MHz) | 1008 | 996 | 1596

## Slide 10: General Specifications
 | Cortex-A7 | Cortex-A9 | Cortex-A15
Cores | 2 | 4 | 4 (+ 4 Cortex-A7)
Max CPU Clock (MHz) | 1008 | 996 | 1596

## Slide 11: Memory Specifications
 | Cortex-A7 | Cortex-A9 | Cortex-A15
L1 Cache (kB) | 32 | 32 | 32
L2 Cache (kB) | 256 | 1024 | 2048
RAM (MB) | 1024 | 2048 | 2048
RAM Type | 432 MHz 32 bit DDR3 | 528 MHz 64 bit DDR3 | 800 MHz 64 bit DDR3
Theoretical Max Bandwidth (MB/s) | 3296 | 8054 | 12 207

## Slide 12: Memory Specifications
 | Cortex-A7 | Cortex-A9 | Cortex-A15
L1 Cache (kB) | 32 | 32 | 32
L2 Cache (kB) | 256 | 1024 | 2048
RAM (MB) | 1024 | 2048 | 2048
RAM Type | 432 MHz 32 bit DDR3 | 528 MHz 64 bit DDR3 | 800 MHz 64 bit DDR3
Theoretical Max Bandwidth (MB/s) | 3296 | 8054 | 12 207

## Slide 13: Memory Specifications
 | Cortex-A7 | Cortex-A9 | Cortex-A15
L1 Cache (kB) | 32 | 32 | 32
L2 Cache (kB) | 256 | 1024 | 2048
RAM (MB) | 1024 | 2048 | 2048
RAM Type | 432 MHz 32 bit DDR3 | 528 MHz 64 bit DDR3 | 800 MHz 64 bit DDR3
Theoretical Max Bandwidth (MB/s) | 3296 | 8054 | 12 207

## Slide 14: LMBench
 | Cortex-A7 | Cortex-A9 | Cortex-A15
Clock Cycle Time (ns) | 0.992 | 1.004 | 0.627
L1 Latency (ns) | 3.02 | 4.02 | 2.51
L2 Latency (ns) | 9.2 | 30.8 | 13.8
RAM Latency (ns) | 58.5 | 119.8 | 104.8
Benchmark suite – memory performance
Focus here is on latencies

## Slide 15: LMBench
 | Cortex-A7 | Cortex-A9 | Cortex-A15
Clock Cycle Time (ns) | 0.992 | 1.004 | 0.627
L1 Latency (ns) | 3.02 | 4.02 | 2.51
L2 Latency (ns) | 9.2 | 30.8 | 13.8
RAM Latency (ns) | 58.5 | 119.8 | 104.8
Best
Worst

## Slide 16: The STREAM Benchmark
Generates array of random numbers (which is stored in RAM) and then performs four types of operations
Test | Equation
Copy | 
Scale | 
Add | 
Triad | 
Test | Equation
Copy | 
Scale | 
Add | 
Triad | 

## Slide 17: STREAM
Chart: Bandwidth (MB/s)
| Copy (MB/s) | Scale (MB/s) | Add (MB/s) | Triad (MB/s)
Cortex-A7 | 1996 | 1444 | 757 | 702
Cortex-A9 | 1329 | 1110 | 1448 | 1290
Cortex-A15 | 6066 | 6114 | 5413 | 5275
STREAM Results
Bandwidth efficiency – percentage of theoretical maximum obtained
Chart: Bandwidth Efficiency (%)
| Cortex-A7 | Cortex-A9 | Cortex-A15
 | 37 | 16 | 47

## Slide 18: pmbw - Parallel Memory Bandwidth Benchmark
Sustained memory bandwidth
Parallel memory bandwidth of multi-core machines
Basic inner loops – sequential scanning and random memory access
12 subtests
Useful to compare to LMBench and STREAM results – potentially greater insight

## Slide 19: pmbw - Parallel Memory Bandwidth Benchmark
One benchmark – 12 subtests
The things that vary:
Operations per loop
Simple (1) vs Unroll (16)
Read vs Write
Sequential Scanning vs Random Pointer Permutation
Scan vs Perm
Pointer-based iteration vs Index-based array access
Ptr vs Index
Bit size of memory transfer
32 vs 64 bits
12 subtests
~ 200 to 300 iterations per subtest
2400 to 3000 observations

## Slide 20: Statistical Analysis
Analysis of Variance (ANOVA)
Are any of the subtest groups different from one another? (statistical significance)
How do the subtests compare to:
Each other?
To STREAM results?
Furthermore: How do these subtests group together?

## Slide 21: Subtest Groupings
Chart: Subtest Grouping
| Random Pointer Permutation | SeqRead32Simple | SeqWrite32 Simple+Unroll | Seq32Unroll+64Simp | Seq64Unroll
Cortex-A7 | 34.7876 | 1555.2507 | 1479.2897 | 1500.2897 | 1708.811
Cortex-A9 | 84.7196 | 1232.4132 | 1458.6814 | 1239.9602 | 1451.6356
Cortex-A15 | 126.5 | 4350 | 4722.4278 | 5100 | 5080

## Slide 22: Subtest Groupings
Chart: Subtest Grouping
| Random Pointer Permutation | SeqRead32Simple | SeqWrite32 Simple+Unroll | Seq32Unroll+64Simp | Seq64Unroll
Cortex-A7 | 34.7876 | 1555.2507 | 1479.2897 | 1500.2897 | 1708.811
Cortex-A9 | 84.7196 | 1232.4132 | 1458.6814 | 1239.9602 | 1451.6356
Cortex-A15 | 126.5 | 4350 | 4722.4278 | 5100 | 5080
Similar profile to STREAM results
Notes: Before the test benchmark routine is called, the array area of each thread is filled with a random cyclic permutation of pointers. Thus for two threads, the allocated array will have the following layout:

## Slide 23: Subtest Groupings
Chart: Subtest Grouping
| Random Pointer Permutation | SeqRead32Simple | SeqWrite32 Simple+Unroll | Seq32Unroll+64Simp | Seq64Unroll
Cortex-A7 | 34.7876 | 1555.2507 | 1479.2897 | 1500.2897 | 1708.811
Cortex-A9 | 84.7196 | 1232.4132 | 1458.6814 | 1239.9602 | 1451.6356
Cortex-A15 | 126.5 | 4350 | 4722.4278 | 5100 | 5080
A9  double A7
A15  only 1.5 times better than A9
Notes: Before the test benchmark routine is called, the array area of each thread is filled with a random cyclic permutation of pointers.
Measured time is the raw bandwidth and latency of a single memory fetch cycle

## Slide 24: Discussion & Analysis
Clear correlation between age of SoC design and memory performance
Existing ARM-based SoCs perform fairly well – A15 is particularly promising
New ARMv8-based SoCs should perform significantly better
Promising for ARM-based SoCs in DSC

## Slide 25: Next Steps & Future Work
HPCG & Graph500 Benchmarks
DIS & HPCC suites
Test newer SoCs (Intel Atom & ARMv8 64 bit)
Database stream management software (DBMS) & other benchmarks

## Slide 26: Cпасибо Questions or Comments?

## Slide 28: Back-up slides

## Slide 29: STREAM
 | Cortex-A7 | Cortex-A9 | Cortex-A15
STREAM |  |  | 
Copy (MB/s) | 1996 | 1329 | 6066
Scale (MB/s) | 1444 | 1110 | 6114
Add (MB/s) | 757 | 1448 | 5413
Triad (MB/s) | 702 | 1290 | 5275
RAM (Theoretical MB/s) | 3296 | 8054 | 12 207
RAM BW Efficiency (%) | 37 | 16 | 47

## Slide 30: Subtest Groupings
Chart: Test Type Grouping
| Perm | ScanRead32Sim | ScanWrite32 S+U | Scan32Un+64Sim | Scan64Un
Cortex-A7 | 34.7876 | 1555.2507 | 1479.2897 | 1500.2897 | 1708.811
Cortex-A9 | 34.7876 | 1232.4132 | 1458.6814 | 1239.9602 | 1451.6356
Cortex-A15 | 126 | 4350 | 4722.4278 | 5100 | 5080
Cortex-A15 1 GHz | 95.0479 | 3526.193 | 4550.8304 | 4043.6309 | 4587.9548

## Slide 31: Random Pointer Permutation
Chart: 
| Cortex-A7 | Cortex-A9 | Cortex-A15
Random Pointer Permutation | 34.7876 | 84.7196 | 126.5

## Slide 32: pmbw Subtest Names
PermRead32SimpleLoop
PermRead32UnrollLoop
ScanRead32PtrSimpleLoop
ScanRead32IndexSimpleLoop
ScanWrite32IndexSimpleLoop
ScanWrite32PtrSimpleLoop
ScanRead32PtrUnrollLoop
ScanRead64PtrSimpleLoop
ScanRead64PtrUnrollLoop
ScanWrite32PtrUnrollLoop
ScanWrite64PtrUnrollLoop
ScanWrite64PtrSimpleLoop

## Slide 33: Random Pointer Permutation C++ Code
// PermRead32SimpleLoop uint32_t p = *array; while( (uint32_t*)p != array ) p = *(uint32_t*)p; | // PermRead32UnrollLoop uint32_t p = *array; while( (uint32_t*)p != array ) { p = *(uint32_t*)p; // ... 14 more times p = *(uint32_t*)p; }

## Slide 34: Data-Intensive Systems (DIS) Stressmark Suite
Comes from an early 2000s DARPA (US military)-led project
Focused on new approaches to solving communication bottlenecks – data-starved systems
Several project groups proposed very different approaches
Approaches ranged from projects with solely software modifications to project groups which proposed and prototyped brand-new architectures, compilers and software

## Slide 35: High Performance Computing Challenge (HPCC)
More recent (again) DARPA-led project
Focused on data-intensive computing
Consists of 7 tests:
Test | HPL | DGEMM | STREAM | PTRANS | RandomAccess | FFT | b_eff
Tests | Floating point rate of execution | Floating point rate of execution (double precision) | Sustainable memory bandwidth | Simultaneous inter-processor communication | Rate of integer random updates of memory (GUPS) | Floating point execution of DP complex 1D DFT | Communication and bandwidth latency

## Slide 36: Graph500 & Green Graph500 Benchmark
Graph500 – benchmark of data-intensive computing
Alternative/competitor to TOP500 List
List is in its infancy
RAM requirements exceed current cluster capacity
Green Graph500
Energy-efficiency data-intensive communication benchmark
Slight modification of Graph500 benchmark

## Slide 37: PMBW Homogenous Subsets - Odroid
Bandwidth |  |  |  |  |  |  | 
Tukey HSDa,b |  |  |  |  |  |  | 
Function Name | N | Subset |  |  |  |  | 
 |  | 1 | 2 | 3 | 4 | 5 | 6
PermRead32UnrollLoop | 196 | 786740597.190892700000000 |  |  |  |  | 
PermRead32SimpleLoop | 196 | 791325508.475172800000000 |  |  |  |  | 
ScanWrite32IndexSimpleLoop | 196 |  | 1746008294.740390000000000 |  |  |  | 
ScanWrite32PtrSimpleLoop | 196 |  | 1758569517.305840300000000 |  |  |  | 
ScanRead32PtrSimpleLoop | 196 |  | 1777096605.063134400000000 |  |  |  | 
ScanRead32IndexSimpleLoop | 196 |  | 1784669478.268580000000000 |  |  |  | 
ScanWrite64PtrSimpleLoop | 196 |  |  | 2499297218.797544000000000 |  |  | 
ScanWrite32PtrUnrollLoop | 196 |  |  | 2666443396.454691400000000 | 2666443396.454691400000000 |  | 
ScanRead64PtrSimpleLoop | 196 |  |  | 2670323598.653305500000000 | 2670323598.653305500000000 |  | 
ScanWrite32PtrMultiLoop | 196 |  |  | 3038413137.236012000000000 | 3038413137.236012000000000 |  | 
ScanRead32PtrUnrollLoop | 196 |  |  | 3158685815.765973600000000 | 3158685815.765973600000000 |  | 
ScanWrite64PtrUnrollLoop | 196 |  |  |  | 3297129002.845765600000000 |  | 
ScanRead32PtrMultiLoop | 196 |  |  |  |  | 4289022493.191038600000000 | 
ScanRead64PtrUnrollLoop | 196 |  |  |  |  |  | 5037445503.439437000000000
Sig. |  | 1.000 | 1.000 | .105 | .150 | 1.000 | 1.000
Means for groups in homogeneous subsets are displayed. Based on observed means. The error term is Mean Square(Error) = 4423590835132220900.000. |  |  |  |  |  |  | 
a. Uses Harmonic Mean Sample Size = 196.000. |  |  |  |  |  |  | 
b. Alpha = .05. |  |  |  |  |  |  | 

## Slide 38: NAS Parallel Benchmarks
Derived from Computational Fluid Dynamics (CFD) simulations
CFD is processor-intensive, but two of the NAS benchmarks have memory-intensive aspects to them

## Slide 39: NAS Parallel Benchmarks
Board SoC | Cortex-A7 | Cortex-A9 | Cortex-A15
Operation Type | Floating Point | Floating Point | Floating Point
Benchmark | Conjugate Gradient, irregular memory access and communication |  | 
Processes | 4 | 4 | 4
Mop/s | 21.04 | 73.72 | 315.15
Mop/s/process | 5.26 | 18.43 | 78.79
Benchmark | Multi-Grid on a sequence of meshes, long- and short-distance communication, memory intensive |  | 
Processes | 4 | 4 | 4
Mop/s | 154.88 | 305.76 | 967.62
Mop/s/process | 38.72 | 76.44 | 241.90

## Slide 40: pmbw – Parallel Memory Bandwidth
14 sub-tests, each run several hundred times (dependent on array size) – lots and lots of info
Used Analysis of Variance (ANOVA) to help make sense of this:
 | Cortex-A7 | Cortex-A9 | Cortex-A15
Sig. difference between means? | p = 0.000 | p = 0.000 | p = 0.000
Effect size |  |  | 
N | 2744 [14*196] | 4200 [14*300] | 4200 [14*300]
Homogenous subsets (test-groupings) | 6 | 6 | 5