## Slide 1: STATUS OF THE DC-280 CYCLOTRON for the Factory of Super Heavy Elements (SHEF)
G.G. Gulbekian, S.N. Dmitriev, Yu.Ts. Oganessian, B.N. Gikal, I.V. Kalagin, S.L. Bogomolov, I.A.Ivanenko, N.Yu.Kazarinov, G.N. Ivanov, N.F.Osipov
PAC, Dubna 2017
FLEROV LABORATORY of NUCLEAR REACTIONS
JOINT INSTITUTE FOR NUCLEAR RESEARCH
Igor Kalagin

## Slide 2: Factory of Superheavy Elements – the main Goals
The Factory will be based on the new DC-280 cyclotron. The cyclotron will produce high intensity ion beams.
DC-280 is being created in the new experimental building of the FLNR.
Synthesis of SHE and studying of their properties;
Search for the new reactions for SHE-synthesis;
Study of chemical properties of SHE;
Because of extremely low (σ<50 fb) cross sections of reactions the experiments require high intensities of primary beams for the best statistics.

## Slide 3
PLAN OF THE FLEROV LABORATORY OF NUCLEAR REACTIONS
The project of the SHEF experimental building
The FLNR main building

## Slide 4
To satisfy the Goals, the DC-280 must have the following parameters of the ion beams:
Ion energy 4÷8 MeV/n
Ion masses 10÷238
Intensities (A~50) >10 pµA
Beam emittance less than 30 π mm·mrad
Efficiency of beam transfer >50%
THE NEW FLNR ACCELERATOR –
THE DC-280 CYCLOTRON
Ion energies correspond to total accelerating potential up to 40 MV

## Slide 5
 | Principles | Expected results
1. | High injection energy of ions (>50 keV/Z) | Decreasing of ion beam emittance (typical injection energy of 15÷20 keV/Z). Effective transportation of ions through injection. Better efficiency of capture into acceleration.
2. | Low magnetic field (<1.5 Т) | Larger beam starting radius. Lower power of the main magnet.
3. | High accelerating voltage (>100 kV) | Higher turns separation. Lower vacuum losses of ions.
4. | Beam extraction by the electrostatic deflector together with the flat-top system | Effective ion extraction. Better beam quality.
Basic principles of the DC-280 design

## Slide 6
Main RF-resonator
Magnet yoke
HV platform N1
(Umax=60 kV)
Electrostatic deflector
(Bender)
Separating magnet
DECRIS-PM
ECR-source
(Umax=20 kV)
Magnet coils
Ion beam extraction
Flat –top resonator
Vacuum pump
Accelerating tube
Actual configuration of the DC-280

## Slide 7
Ion sources | DECRIS-PM - 14 GHz on the 1-st HV platform Superconducting ECR on the 2-nd HV platform (developing stage)
Injection energy | Up to 80 keV/Z
A/Z range | 4÷7.5
Energy | 4÷8 MeV/n
Magnetic field level | 0.6÷1.35 T
K factor | 280
Dee voltage | 2x130 kV
RF power consumption | 2x30 kW
Flat-top dee voltage | 2x13 kV
Flat-top power consumption | 2x2 kW
Main design parameters of the DC-280

## Slide 8
ION | Z | Beam Intensity from ECR |  | HV platform N | Efficiency of acceleration | Expected beam intensities of (4÷8) MeV/n ions on targets pps
 |  | eA | pps |  |  | 
20Ne | 3 | 150 | 3.1014 | 1 | 50% | 1.5·1014
40Ar | 7 | 300 | 3.1014 | 1 | 50% | 1.5·1014
48Са | 7/8 | 160 | 1.1014 | 1 | 50% | 6.2·1013
50Ti | 8/9 | 75 | 5.1013 | 1 | 50% | 2.6.1013
54Cr | 9 | 125 | 8.1013 | 1 | 50% | 4.1013
58Fe | 9/10 | 125 | 8.1013 | 1 | 50% | 4·1013
64Ni | 10/11 | 125 | 8.1013 | 1 | 50% | 4·1013
70Zn | 11/12 | 100 | 5.1013 | 1 | 50% | 2,5.1013
136Хе | 22/23 | 150 | 4.1013 | 1 | 50% | 2·1013
209Bi | 34/35 | 15 | 2,2.1012 | 2 | 60% | 1·1012
238U | 39/40 | 1 | 1,5.1011 | 2 | 60% | 1.1011
Expected beam parameters of the DC-280

## Slide 9
N | Item
1 | Magnetic system
2 | RF system
3 | Beam injection system
4 | Beam extraction system
5 | Beam transport system
6 | Diagnostic system
7 | Vacuum system
8 | Water cooling system
9 | Control system
Main systems of the DC-280

## Slide 10: Magnetic system of ДЦ-280
Size of magnet yoke LхWхH | 8.76х4.08х4.84 m3
Pole diameter | 4 m
Gap between central plugs | 400 mm
Valley/hill gap | 500/208 mm/mm
Magnet weight | 1100 t
Magnet power | 300 kW
Maximal current | 905 A
Magnetic field level | 0.6÷1.35 T
DC-280 magnet at the FLNR, February 2017
Magnet at the NKMZ, Ukraine (2014)
Magnet assembling (November 2016)
DC-280- isochronous cyclotron
Main coils made in N&V, Romania (2016)

## Slide 11
Magnet trimming coils
Number of radial trimming coils | 11
Number of azimuthal trimming coils | 8
Block of radial trimming coils
(EVPU, Slovakia)
Blocks of azimuthal trimming coils (GKMP, Bryansk, Russia)
Radial trimming coils
Azimuthal trimming coils

## Slide 12
Vacuum chamber of the DC-280 magnet
Vacuum chamber has been manufactured at the NKMZ plant.
Vacuum tests have been made at the FLNR (2016)
Working vacuum is 10-7 mBar

## Slide 13
Magnetic field measurements
The magnetometer with 14 Hall probes has been developed at the FLNR and was manufactured at the SPA “ATOM”, Dubna. Radial and azimuthal motions are carried by thepneumatic engines with using toothed belt for azimuthal stepping. Measuring accuracy of 10-4.
Actual period of magnetic field measurements: June - August of 2017.
The delay in the beginning of the measurements has been cased by the delay in obtaining permission from federal supervisory authorities on connection the magnet to the power supply.
Magnetometer
Bottom sectors
Top sectors
Example: 3D field map
Toothed belt

## Slide 14
3Frf
Frf
RF system
Frf=7.32÷10.38 MHz
Fft=21.96÷31.14 MHz
The main dee (EVPU, Slovakia)
The RF resonator at the FLNR
(ZAVKOM, Tambov, Russia)
Internal details of the resonator
The RF generators have been made in the QEI Corporation, NJ, USA
Configuration of the DC-280

## Slide 15
Ion beam
Magnet yoke
Bender
±15 kV
HV platform
Umax=60 kV
Beam injection system
Focussing solenoids
Working vacuum in injection is 5·10-8 mBar
Vacuum volumes made by “Vacuum Praha”, Czech Republic
NEC,USA
Median plane
Inflector
“Vacuum Praha”
Buncher

## Slide 16: Beam injection system
The HV platform N1 (May 2017)
Internal focusing solenoids have been installed to the cyclotron center (May 2017)
The magnet with the base platform for injection
Magnetic elements for the injection made in EVPU, Slovakia

## Slide 17
ECR-ion sources
Ion spectrum of DECRIS-PM (March 2017)
The new ECR-ion source DECRIS-PM (14 GHz)
for the 1-st HV platform .
(FLNR and “ITT-Group”, Moscow).
The FLNR has experience in developing and creation of DECRIS-SC and DECRIS-SC2 (18 GHz). The experience will be used for developing the new superconducting ECR for the 2-nd HV platform.

## Slide 18
Beam extraction system
Electrostatic deflector
Focusing magnetic channel
Extraction radius of Rext=1.79 m
Ion beam

## Slide 19
Electrostatic deflector
Magnetic channel
Length of electrostatic deflector | 1.3 m
Deflector voltage | 80 kV
Length of the magnetic channel | 0.9 m
Gradient of the magnetic channel | 4.6÷8.4 T/m
The magnetic channel has been produced at the Institute for Nuclear Research and Nuclear Energy of the Bulgarian Academy of Science.
Electrostatic deflector is being produced in the same Institute.

## Slide 20
Bending magnet ±50
Quadrupole lenses
MAX beam power ~2.5 kW
Beam transport system
Area of
experimental setups
Vacuum volumes of channels: “Vacuum Praha”, Czech Republic
Working vacuum is 10-7 mBar
Beam diagnostics: INR&NE of the Bulgarian Academy of Science
Ion beam

## Slide 21
TM±50 bending magnet
(NKMZ, Ukraine)
The triplet of quadrupole lenses 11К30-700
(N&V, Romania)
Magnetic optics
Quadrupole doublet and TM±50 at the DC-280 hall

## Slide 22
Water cooling system
The water cooling system was developed at the FLNR (equipment suppliers: Russia, Italy, Germany)

## Slide 23
Control system
The control system based on FLNR developments and LabVIEW

## Slide 24
Experimental area ~1000 m2 (3 halls)
Plan of the 1-st floor of the SHEF
Notes: 24

## Slide 25
Schedule
Increasing of the FLNR staff for the SHEF
The JINR Directorate granted to the FLNR additional wages fund for 2017.

## Slide 26
THANKS FOR YOUR ATTENTION!
The building of the SHEF
June 2017
The outline sketch of the building (2012)

## Slide 27
Working diagram of the DC-280