## Slide 1
46th PAC for Nuclear Physics
June, 14, 2017, JINR, Dubna
Targets, Separators, Detector Units for Superheavy Elements Factory
A.G. Popeko
Flerov Laboratory of Nuclear Reactions,
Joint Institute for Nuclear Research

## Slide 2
184
114
Og
Ts
Nh
2016
Fl
Mc
Lv
Decay chains

## Slide 3: Superheavy element factory – the goals
Synthesis and study of properties of superheavy isotopes
Chemistry of new elements
Fusion and multi-nucleon transfer reactions
Mass-spectrometry and nuclear spectroscopy of SH nuclei
Laser spectroscopy of heavy atoms.

## Slide 4
Targets

## Slide 5: Target isotopes
Isotope | Enrichment % | Isotope | Enrichment %
232Th | 100 | 244Pu | 98.6
233U | - | 243Am | 99.9
238U | 99.3 | 245Cm | 98.7
237Np | 99.3 | 248Cm | 97.4
239Pu | - | 249Bk | >95
240Pu | 99.8 | 249Cf | 97.3
242Pu | 99.98 | 251Cf | 36
Isotope separators are necessary !

## Slide 6: Isotope reactors
HFIR, ORNL, Oak Ridge, USA, 85 MW
CM-3, IAR, Dimitrovgrad, RF, 100 MW

## Slide 7: Targets I – material availability 22 mg of 249Bk, 1 year at HIFR ORNL

## Slide 8: Transmission & yield of 254No 208Pb(48Ca,2n)254No (FWHM=10.0 MeV→1.37 mg/cm2, σ =0.583 mg/cm2)
Targets II – optimization for the highest production rate

## Slide 9: Targets III – radiation safety
248Cm @ SHIP
(S. Hofmann)
249Cf @ DGFRS

## Slide 10
Targets IV – destruction
Heating and melting;
sputtering;
radiation damage.

## Slide 11: Targets V – reduction of heating
ø5 cm
ø10 cm
ø30 cm
ø60 cm →
Target: 2 μm Ti + 0.5 mg/cm2 U3O8
Beam: 48Ca, 1 pμA → 20 W/cm2 → T = 1600K

## Slide 12: Target block design (G.N. Ivanov)
old
new
Ø = 120, 1500 r.p.m. synchronous
Beam wobbler or scanner,
Segmented beam diafragm
Is in use at GFS, SHELS, MASHA
Ø = 480, 1500 r.p.m. synchronous,
e-beam & optical diagnostic,
water cooling

## Slide 13: Separators

## Slide 14: Analyzed reactions

## Slide 15: Conclusion I Pure magnetic vacuum systems will not work
48Ca(E1/2= 236MeV) + 248Cm(300μg/cm2, CmO2) → 296116*

## Slide 16: Conclusion II Technical requirements
 | Air-free | Gas-filled
Electric rigidity | < 10 MV | ---
Magnetic rigidity | < 1.0 T×m | < 3.1 T×m
Field gradients in quadrupoles | < 5 T/m | < 15 T/m

## Slide 17: Conclusion III:
Universal gas-filled separator QDQQD
performs focusing in impulse & charge spaces,
is manufacturing
Velocity selector SHELS performs focusing in charge space, in test operation
Gas-filled pre-separator
in project

## Slide 18: Gas-filled separator:
Pros:
Can provide the highest efficiency
Provides additional cooling due to filling gas
Cons:
Is not applicable for symmetric reactions

## Slide 19: Gas-filled separator, the tasks:
asymmetric complete fusion reactions
multi-nucleon transfer reactions
nuclear spectroscopy @ focal plane

## Slide 20
Separator | DGFRS | GARIS | RITU | BGS | TASCA | SHANS
Configuration | DQhQv | DQhQvD | QvDQhQv | QvDhD | DQhQv | QvDhQvQh
Deflection angle | 23º | 45º+10º | 25º | 70º | 30º | 52º
Bρ (max/T∙m) | 3.1 | 2.15 | 2.2 | 2.5 | 2.4 | 2.9
Length (m) | 4.0 | 5.75 | 4.7 | 4.6 | 3.5 | 6.5
Dispersion (mm/% Bρ) | 7.5 | 9.7 | 10.0 | 20.0 | 9.0 | 7.3
GF-separators

## Slide 21: New gas-filled separator GFS-2

## Slide 22: Optical elements of GFS-2
Effective length | 460 mm
Bore diameter | 150 mm
Maximum field gradient | 13.2 T/m
Effective length | 600
Bore diameter | 300 mm
Maximum field gradient | 5.5 T/m
Gap | 132 mm
Deflection angle | 300
Radius of curvature | 1.8 m
Maximum field | 1.8 T
Face pole rotation angle | -70
Rear pole rotation angle | 43.50
Gap | 132 mm
Deflection angle | 100
Radius of curvature | 1.8 m
Maximum field | 1.8 T
Face pole rotation angle | 00
Rear pole rotation angle | 100
Magnetic quadrupole 1
Magnetic quadrupole 2 & 3
Magnetic dipole 1
Magnetic dipole 2

## Slide 23
GFS-2, the coils

## Slide 24: GFS-2, manufacturing progress

## Slide 25: Arrangement of GFS-2 at the beam line No3

## Slide 26: Velocity selector, the tasks:
symmetric & asymmetric complete fusion reactions;
multi-nucleon transfer reactions;
nuclear spectroscopy @ target & focal plane.

## Slide 27
Separator for Heavy ELement Spectroscopy (SHELS)

## Slide 28
Preseparator & gas-catcher, RSC-chamber:
chemistry
fusion and multi-nucleon transfer reactions
mass-spectrometry and nuclear spectroscopy
laser spectroscopy of heavy atoms

## Slide 29: Gas-filled pre-separators
QvDQh
Superconducting

## Slide 30: Gas-Filled Pre-separator QVDH
Dipole D1 |  | 
 | warm | super
Bending angle | 40o | 40o
Bending radius | 1.8 m | 1.0 m
Maximum field | 1.8 T | 3.3 T
Field inhomogeneity factor n1 | -1.262 | -1.249
Front & rear pole face rotation angles | -35o | -20o
Quadrupole Q1 (vertical) | 
Effective length | 600 mm
Bore diameter | 200 mm
Maximum field gradient | 13.5 T/m

## Slide 31: Detectors

## Slide 32: Focal plane DSS-Detectors (Micron Semiconductors, UK)
48 × 128 strips
6144 pixels
128 × 128 strips
16384 pixels
Detector box

## Slide 33
GABRIELA - Gamma Alpha Beta Recoil Investigation with the Electromagnetic Analyser
New focal plane detector GABRIELA

## Slide 34: 50Ti beam intensity – 3×1012 pps. 50Ti + 208Pb = 256Rf + 2n
3He – neutron detector system
ε(252Cf) = 40%
Neutron multiplicity measured for spontaneous fission of 256Rf
TKE spectra for S.F. of 256Rf isotope
Notes: For the synthesis of elements heavier than 118, the beams of ions heavier than Ca-48 are needed. In cooperation with our colleagues from France the Ti-50 ions were accelerated at the U400. First experiments were dedicated to the measurement of the average number of prompt neutrons from spontaneous fission of Rf, produced in 50Ti+208Pb reaction using the modernized VASSILISSA separator He-3 neutron detector. These set-ups were developed in accordance with the DRIBS-III project. The average number of neutrons was found to be 4.47 n/SF. These measurements are of special interest for understanding properties of SHE and for their search in nature.

## Slide 35: Data taking
Home made
ORNL

## Slide 36
THANK YOU FOR YOUR ATTENTION !