## Slide 1: Proposal for the extension of the project “Design and development of the tagged neutron method for determination of the elemental structure of materials and nuclear reaction studies” project TANGRA TAgged Neutrons & Gamma-Rays
Theme: 03-4-1128-2017/2019
“Investigations of neutron nuclear interactions and properties of the neutron”
Project Leader: Yu.N. Kopatch
Deputy: V.M.Bystritsky

## Slide 2: Tagged Neutrons Method – TNM
Main components:
Neutron generator with a position sensitive detector of -particles
Shielding
Detectors of -rays / neutrons
Sample
d + t  4He (3.5МeV) + n (14.1МeV)
Main advantages of the method:
Precise determination of the number of neutrons hitting the target: each neutron is “tagged” by the -detector
Information about space and time location of the interaction of the neutron with a target (X,Y-coordinates are given by the pixels of the -detector; Z,t-coordinates are defined by the time-of-flight)
Due to the selection of a small space-time volume of interaction (voxel) the contribution of background is significantly reduced
The method allows to identify different elements and substances using their characteristic gamma-rays
1
2
3
4

## Slide 3: Aims of the project
Development of the tagged neutron method for identification of a wider range of elements and substances
Using tagged neutron beams for experimental investigations in the field of fundamental nuclear physics
Development of methods to study the elemental composition of soils and minerals to determine the content of various elements
Development of a database on reaction cross sections for interaction of neutrons with energy 14.1 MeV with nuclei and on the characteristic gamma lines
Investigation of reactions (n,n`)
using the tagged neutrons method.
Design and construction of gamma and neutron detectors with improved timing and energy characteristics for use in intense neutron fields.
Development of algorithms for the analysis of experimental data coming from the detectors of neutron and gamma radiation.
Investigation of reactions (n,2n`), (n,n`) using the tagged neutron method.
2. Applied research
1. Basic research
3. Methodical research

## Slide 4
№ | Name of main works and stages | Work periods (year, quarter) |  | 
 |  | Beginning | End | Compl
1 | Conduction of test measurements with the neutron generator and detection system “Romashka” to determine the parameters and structure of the shielding | 2013, IV | 2014, I | 
2 | Development of the combined shielding for gamma-radiation and neutron detectors | 2014, I | 2014, II | 
3 | Conduction of measurements of characteristic gamma-spectra for various elements. Creation of data base for element identification. | 2014, II | 2016, IV | 
4 | Conduction of experiments on measurements of angular correlations of gamma-ray emission in the reactions of neutron inelastic scattering on light nuclei. | 2014, IV | 2016, IV | 
5 | Conduction of experiments on measurement of cross-sections in the (n,2n), (n,n`) reactions. | 2015, I | 2016, IV | ▬
6 | Studies of the Martian soil model. | 2015, I | 2016, IV | 
7 | Development of the technique for studies of the elemental composition of soils and minerals. | 2014, I | 2016, IV | 
Main works and stages in the framework of the project
in 2014-2016

## Slide 5: Main results obtained in 2014-2016: 1. Measurements of direct 14 MeV neutron beam suppression factor for different materials
Materials: Fe, Pb, BPE
Detectors: NaI, BGO, Stilbene, Ne-213
V. M. Bystritsky et al, Physics of Particles and Nuclei Letters 12(2) (2015)
Neutron and gamma components are measured separately

## Slide 6: Main results obtained in 2014-2016: 2. Measurement of angular distribution of 4.43 MeV -rays from 12C(n,n’) reaction
a=2.470.1
b=2.04 0.12
Anderson et al:
a=1.750.18
b=1.20 0.31
Yu.N. Kopatch et al, Reported at ISINN-23, Dubna (2015)
V. M. Bystritsky et al, Physics of Particles and Nuclei Letters (2016)
Reported at the 43rd PAC meeting in 2016

## Slide 7: Main results obtained in 2014-2016: 3. Determination of the elemental composition of friable ores
C.Hramco et al, ISINN-24 Dubna, May 24–27, 2016,JINR, E3-2017-8, p. 157

## Slide 8: Main results obtained in 2014-2016: 4. Determination of the relative humidity of coke (fuel)
D.Grozdanov et al., Physics of Particles and Nuclei Letters (2016), submitted
Neutron capture
Neutron inelastic scattering

## Slide 9: Main results obtained in 2014-2016: 5. Construction of an experimental stand for the testing of devices of nuclear planetology
Curiosity
A.A. Vostrukhin et al, Physics of Particles and Nuclei Letters (2016)
Reported at the 43rd PAC meeting in 2016

## Slide 10: Main results obtained in 2014-2016: 6. Construction of a silicon two-dimensional position-sensitive fast neutron detector for beam profile measurement
F.Aliev et al, Ireported at SINN-25 Dubna, May 22–26 2017
2D detector, made of 4 double sided
stripped position sensitive Si detectors
Each Si detector consists of 32x32 strips ~1.8 mm thick
Size of one detector: 60x60mmm
Total size: 120x120 mm
Thickness: 300 mkm
Neutron detection efficiency: ~0.8%
At this stage each 8 strips are grouped together
forming a matrix 8x8 with a pixel size of ~1.5x1.5 cm

## Slide 11
List of Publications
I.N. Ruskov, Yu.N. Kopatch, V.M. Bystritsky, V.R. Skoy et al., TANGRA-Setup for the Investigation of Nuclear Fission Induced by 14.1 MeV Neutrons, Physics Procedia 64 (2015) 163-170, ISSN:1875-3892, Elsevier, http://www.sciencedirect.com/science/article/pii/S1875389215001388.
Mahmoud I. Abbas, M.S. Badawi, I.N. Ruskov, A.M. El-Khatib, D.N. Grozdanov, A.A. Thabet, Yu.N. Kopatch, M.M. Gouda, V.R. Skoy, Calibration of а single hexagonal NaI(Tl) detector using a new numerical method based on the efficiency transfer method, Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment, 771 (2015) 110-114, http://www.sciencedirect.com/science/article/pii/S0168900214012133.
Быстрицкий В.М., Валкович В., Грозданов Д.Н., Зонтиков А.О., Иванов И.Ж., Копач Ю.Н., Крылов А.Р., Рогов Ю.Н., Русков И.Н., Сапожников М.Г., Ской В.Р., Швецов В.Н., Многослойная пассивная защита сцинтилляционных детекторов на основе кристаллов BGO, NaI(Tl) и стильбена, работающих в интенсивных нейтронных полях с энергией 14,1 МэВ, Письма в ЭЧАЯ, Том:12, № 2, Страницы: 486-504, eISSN:1814-5973, Изд: ОИЯИ, http://www1.jinr.ru/Pepan_letters/panl_2015_2/18_bystr.pdf.
V.M. Bystritsky, V. Valkovic, D.N. Grozdanov, A.O. Zontikov, I.Zh. Ivanov, Yu.N. Kopatch, A.R. Krylov, Yu.N. Rogov, I.N. Ruskov, M.G. Sapozhnikov, V.R. Skoy, V.N. Shvetsov, Multilayer passive shielding of scintillation detectors based on BGO, NaI(Tl), and stilbene crystals operating in intense neutron fields with an energy of 14.1 MeV, Physics of Particles and Nuclei Letters 12(2) (2015) 325-335, MAIK Nauka/Interperiodica; http://link.springer.com/article/10.1134/S1547477115020089.
D.N. Grozdanov, A.T. Issatov, Yu.N. Kopach, V.R. Skoy, S.I. Negovelov, I.N. Ruskov, Energy and Time Resolution of Gamma-ray Detectors, Proc. of ISINN-22, http://isinn.jinr.ru/proceedings/isinn-22/pdf/grozdanov.pdf.
В.М.Быстрицкий, Д.Н. Грозданов, А.О. Зонтиков, Ю.Н. Копач и др., Угловое распределение γ-квантов с энергией 4,43 МэВ, образующихся при неупругом рассеянии нейтронов с энергией 14,1 МэВ на ядрах, письма в ЭЧАЯ, 2016, т.13, №4(202), с. 793-807
V.M. Bystritsky et al, The angular distribution of γ-rays with energy 4.438 MeV produced in the inelastic scattering of neutrons with energy of 14.1 MeV on 12C, submitted to Physics of Particles and Nuclei Letters (2016).
Вострухин А.А., Головин Д.В., Дубасов П.В. и др., Экспериментальный стенд для испытания приборов ядерной планетологии, Physics of Particles and Nuclei Letters (2016).
+ 17 conference reports

## Slide 12: TANGRA collaboration meetings in 2016
TANGRA meeting 20.10.2016
JINR
VNIIA (Moscow, Russia)
Diamant (Dubna, Russia)
Institute Ruđer Bošković (Croatia)
INRNE (Sofia, Bulgaria)
TANGRA meeting 8-9.12.2016
JINR
VNIIA (Moscow, Russia)
MSU (Moscow, Russia)
Diamant (Dubna, Russia)
Institute Ruđer Bošković (Croatia)
University of Alexandria (Egypt)
CNR-IFP (Milano, Italy)
BHU-DP (Varanasi, India)
TINT (Bangkok, Thailand)
INRNE (Sofia, Bulgaria)
ENU FPTS (Astana, Kazakhstan)
ICH ASRM (Kishinev, Moldova)
IGG ANAS (Baku, Azerbaijan)
UNS (Novi Sad. Serbia)

## Slide 13: TANGRA in 2017 - 2019
Participants:
Frank Laboratory of Neutron Physics, JINR, Dubna, Russia
Veksler and Baldin Laboratory of High Energy Physics, JINR, Dubna, Russia
Dzhelepov Laboratory of Nuclear Problems, JINR, Dubna, Russia
Laboratory of Radiation Biology, JINR, Dubna, Russia
N.L. Dukhov All-Russian Automation Research Institute, Moscow, Russia.
Laboratory for Nuclear Analytical Methods, Institute Ruđer Bošković, Zagreb, Croatia
Institute for Nuclear Research and Nuclear Energy, Bulgarian Academy of Sciences, Sofia, Bulgaria
New project members
Lomonosov Moscow State University, SINP, Moscow, Russia.
Banaras Hindu University, Varanasi, India
University of Alexandria, Egypt
Horia Hulubei National Institute for R&D in Physics and Nuclear Engineering (IFIN-HH, Bucharest, Romania)

## Slide 14: Plans for 2017-2019
Task | Years
Measurements of the n’- angular and energy correlations in the inelastic scattering of 14 MeV neutrons on carbon | 2017
Measurements of the 14 MeV neutron inelastic scattering reaction on other light elements (O, N, Be) | 2017-2018
Measurement of cross-sections in the (n,2n), (n,n`) reactions | 2018-2019
Further development of the elemental analysis using the tagged neutrons method | 2017-2019
Development of the Mone Carlo methods for simulations of experiments for the element and isotopic composition analysis | 2017-2019
Study of radiation damage in scintillators and silicon photodetectors by neutron irradiation | 2017-2019
Studies of the Martian soil model | 2017-2019
Construction and testing of the position sensitive 2D fast neutron silicon detector | 2017
Construction of a new gamma spectrometer based on 24 BGO scintillator detectors | 2017

## Slide 15: Plans for 2017-2019 New gamma-ray detectors, based on BGO crystals
Number of detectors: 24
Total size: 89x280 mm
Size of BGO crystals: 76x65 mm
PMT type: R1307
Energy resolution @662 keV: ~11 %
Energy resolution @4.4 MeV: ~4.5 %
Time resolution @4.4 Mev: ~3.5 ns
Modular design allowing construction of different geometries
Side view
Top view

## Slide 16: Plans for 2017-2019 Measurements of differential cross sections of the inelastic scatering of 14.1 MeV neutrons on different materials
12C
27Al
208Pb
209Bi
56Fe
28Si, Eg = 1.8 MeV
24Mg, Eg = 1.4 MeV
12C, Eg = 4.4 MeV
16O, Eg = 6.1 MeV
Angular distributions of gamma-rays: preliminary results obtained with NaI detectors
New samples

## Slide 17: Plans for 2017-2019 Development of theoretical models describing angular correlations in the inelastic scattering on 14.1 MeV neutrons on nuclei
N.Fedorov, reported at ISINN-25, May 22-26 2017, Dubna
N.Fedorov, Master Thesis, 2017

## Slide 18: Plans for 2017-2019 Investigation of the (n,2n`) and (n,n`) – reactions using the tagged neutron method
Investigation of the reaction 10B(n,2n)9B  p + 8Be.
Aim: Obtaining information about the low-lying levels of the unstable nucleus 9B
Method: Measurement of the energies of two neutrons using time of flight and calculation of missing-mass spectrum for 9B.
Using high efficiency DEMON detectors with n-gamma separation capability

## Slide 19
Required resources in 2017-2019
Description of units and systems, resources, funding sources |  |  | Cost of units (k$). Resource requirements. | Proposals for distribution of funds and resources. |  | 
 |  |  |  | 2017 | 2018 | 2019
Main units and equipment | 1. Construction of the 24-section gamma spectrometer based on BGO detectors |  | 30 | 30 |  | 
 | 2. Design and development of a position-sensitive Si neutron detector |  | 10 | 10 |  | 
 | 3. Purchase of neutron detectors |  | 70 | 20 | 20 | 30
 | 4. Purchase of high resolution gamma detectors |  | 120 |  | 60 | 60
 | 5. Design and development of digital electronics |  | 80 | 20 | 30 | 30
 | 6. Purchase of targets |  | 50 | 10 | 20 | 20
 | 7. Neutron generator ING-27 from VNIIA |  | 100 | - | - | -
Travel expenses |  |  | 90 | 30 | 30 | 30
Required resources | Norm-hour | FLNP workshops | 600 | 200 | 200 | 200
 |  | Design bureau | - | - | - | -
 |  | Reactor | - | - | - | -
Funding sources | Budget | Theme 1104 | 450 | 120 | 160 | 170
 | Contribution from VNIIA |  | 100 |  |  | 

## Slide 20: Summary
The project aimed at the experimental investigations in the field of basic and applied nuclear physics using tagged neutron beam is proposed to be extended in the framework of the theme 1128 (FLNP) with participation of 4 JINR laboratories and 7 external institutes.
Total funding of 450 k$ is requested for 3 years.
A large part of the equipment including ING-27 neutron generator (contribution by VNIIA) is already available.
Good experience of the teams participating in the project assures its successful realization.

## Slide 21: Thank you for your attention