## Slide 1
First experiments on deep ionization of Ir, Ce and Xe atoms
in local ion trap at JINR
Petersburg Nuclear Physics Institute, St. Petersburg, Russia
V. P. Ovsyannikov, E. D. Donets, E. E. Donets, D. E. Donets, S. I. Tytynnikov, V. I. Stegailov,
A. Yu. Ramsdorf, A. Yu. Boytsov, D. N. Rassadov
A. V. Nefiodov
Joint Institute for Nuclear Research, Dubna, Russia
A. A. Levin
MaMFIS Group, Hochschulstr. 13, D-01069 Dresden, Germany

## Slide 2
Production of highly charged ions in electron beams (history)
Electron Beam Ion Source (EBIS),
E. D. Donets, Dubna, 1967
Electron Beam Ion Trap (EBIT),
M. Levine, R. Marrs, LLNL, 1986
Ltrap= 0.7 – 1.5 m, je ~ 500 A/cm2
Ltrap= 2 cm,
je ~ 2 kA/cm2
K, cathode
W, focusing (Wehnelt) electrode
A, anode
S1, S2,…, Sn, sections of drift tube
C, collector
E, extractor
z, axis of electron beam
je , effective electron current density
Ltrap , trap length
Main Magnetic Focus Ion Source
(MaMFIS)
Ltrap= 1 mm
je > 10 kA/cm2

## Slide 3
Main Magnetic Focus Ion Source (MaMFIS)
Electron current density je is the key quantity, because it determines
the rate for production of highly charged ions

## Slide 4
Operation principle of MaMFIS (Single Focus)
C, cathode
W, focusing (Wehnelt) electrode
A, anode
z, axis of electron beam
B(z), magnetic field distribution
F, magnetic focuses (local ion traps)
Electron beam trajectories for
single-focus electron optics (theoretical estimation)
Radial (left fig.) and axial (right fig.) distributions of electron current density je near focus point F
The electron current density in a single focus can be extremely high!

## Slide 5
Operation principle of MaMFIS (Three Focuses)
Axial distribution of
electron current density
on the length of 1 mm
near focuses
C, cathode
W, focusing (Wehnelt) electrode
A, anode
D, drift tube
z, axis of electron beam
B(z), magnetic field distribution
F1, F2, F3, magnetic focuses (local ion traps)
Effective electron current density je ~ 20 kA/cm2
Local ion traps in
a rippled electron beam

## Slide 6
MaMFIS-10 versus LLNL superconducting EBIT
M.A. Levine, R.E. Marrs,
J.R. Henderson, D.A. Knapp
and M.B. Schneider,
Phys. Scripta T22, 157 (1988)
LLNL EBIT
V.P. Ovsyannikov and A.V. Nefiodov,
Nucl. Instr. Meth. B 370, 32 (2016)
MaMFIS-10
Ee b 10 keV
Ie = 50 mA
First run: Justus-Liebig-University Giessen, 2013
X-ray spectra from cathode materials

## Slide 7
MaMFIS-10: Estimation of electron current density
X-ray emission due to radiative recombination into the M-shell of Ir ions (experiment)
Charge-state distributions of Ir ions for different electron current density (computer simulation)
Electron current density is estimated to be je ~ (10 – 20) kA/cm2

## Slide 8
MaMFIS family developed until now
MaMFIS-10
Ee b 10 keV
MaMFIS-4
Ee b 4 keV
MaMFIS-8
Ee b 8 keV
MaMFIS-30
Ee b 30 keV
Not yet tested

## Slide 9
MaMFIS-40 at JINR in Dubna
Project parameters:
Electron energy Ee b 35 keV
Electron current density je b 20 kA/cm2
Electron current Ie b 50 mA (DC-mode)
First assembling of MaMFIS-40D
Realized parameters:
Ee b 40 keV
je b 20 kA/cm2
Ie b 50 mA
Assembling for extraction mode
Aim of project:
Development of MaMFIS technology for production of highly charged ions of
heavy elements

## Slide 10
Permanent magnet focusing system
Focusing permanent magnets
Focusing permanent magnets on ionization chamber
Magnetic field distribution

## Slide 11
Electron gun and its characteristics
Volt-Ampere characteristics of electron guns (EG)
Electron beam trajectories
vs. Electron energy Ee
Cathode assembly of electron gun

## Slide 12
Vacuum
Vacuum volume < 1 litre
Baking procedure
During operation vacuum ranges
from 10-9 to 5×10-8 mbar

## Slide 13
X-ray spectroscopy
Experimental scheme
Radiation spectrum of cathode materials
Efficiency of registration

## Slide 14
Radiative recombination continuum
RR spectrum for different Ee
RR spectrum for Ee= 22.5 keV
Cathode materials (Ir & Ce)

## Slide 15
Radiative recombination continuum
RR spectrum of xenon
RR spectrum of bismuth (blue curve) compared to that of cathode materials (red curve)
Injected materials (Bi & Xe)

## Slide 16
Applications
Atomic physics (X-ray spectroscopy and ion-atom collisions)
X-ray astrophysics and solar physics
Plasma physics (magnetic fusion diagnostics)
Interaction of highly charged ions with surface (secondary electron and ion emission)
Secondary ion mass spectrometry
Nanostructuring
Advantages:
Highest ionization factor among the ion sources
available around the world
Minimum confinement time
High-frequency operation
Disadvantage:
low intensity in pulse
Features and applications of MaMFIS

## Slide 17
Penning Trap experiments
Future Penning Trap Experiments
at GSI / FAIR – The HITRAP and MATS Projects
K. Blaum1,2 and F. Herfurth1 for the HITRAP and MATS Collaboration
1GSI Darmstadt, 2Johannes Gutenberg-University Mainz
MaMFIS as ion source for high-precision mass measurements
Resolution:
Intensity of ions > 1 ion/s
MaMFIS technology perfectly fulfills the requirements
MaMFIS is a very efficient Charge Breeder
with trap capacity of 105 – 106 charges, in particular, for short half-life radionuclides
“The radioactive beam intensity spans … from a few to over 1010 ions/s.”
F. Wenander, Charge breeding of radioactive ions with EBIS and EBIT,
Int. Symposium on Electron Beam Ion Sources and Traps,
April 7th-10th 2010, Stockholm, Sweden

## Slide 18
MaMFIS:
Ee ~ 10 keV Ee ~ 40 keV
je ~ 20 kA/cm2 je ~ 200 kA/cm2
ne ~ 2×1013 cm-3 ne ~ 1014 cm-3
High-density microplasma research
Joel Clementson, LLNL

## Slide 19
High-frequency accelerators
Accelerated ion | 16O5+ | 20Ne6+,7+ | 40Ar12+,13+ | 56Fe17+,18+ | 84Kr25+,26+ | 132Xe36+ ÷ 39+ | 184W42+ ÷ 46+ * | 209Bi48+ ÷ 53+
A/Z | 3.2 | 3.67, 2.86 | 3.33, 3.08 | 3.29, 3.11 | 3.36, 3.23 | 3.38 ÷ 3.67 | 4 ÷ 4.38 | 3.94 ÷ 4.45
Yield, ions/s | 7107 | 8107 | 9107 | 108 | 3108 | 4108 | 4108 | 4108
Low-intensity, high-charge state ion beams
for special applications
Ion source of MaMFIS-10 type:
expected yield of Kr25+ ~ 108 ions per second

## Slide 20
Nanostructuring
http://yebisu.ils.uec.ac.jp/surface.html
Prof. Dr. Marika Schleberger
University Duisburg-Essen
(Dresden EBIT)
Basic research – University of California, Berkeley
Livermore EBIT was moved to Berkeley in 2001
Basic idea – R. Schmieder, 1991

## Slide 21
Summary
Novel method for production of highly charged ions in a rippled electron beam is developed and confirmed experimentally at electron energies Ee b 22.5 keV
Electron current density of about 20 kA/cm2 is achieved
X-ray radiation from highly charged ions of Ir67+ and Xe50+ is detected
Method allows one to produce any ions of arbitrary elements of the periodic table up to U92+ ions in simple compact devices
X-ray spectroscopy of all elements of the periodic table is feasible

## Slide 22
Acknowledgements
The authors express deep gratitude to
A. A. Smirnov and A. A. Karpukhin for help in the x-ray spectroscopic measurements,
Mueller for giving opportunity to test the first MaMFIS in Institute for Atomic and Molecular Physics
at Justus-Liebig-University Giessen,
O. K. Kultashev for his contribution to creation of electron optics,
All members of Krion Group of Joint Institute for Nuclear Research in Dubna, who help in experiments
THANK YOU FOR YOUR ATTENTION !