## Slide 1
Scientific-methodical Department LHEP
14.03.2016г.
Beam and Target Optimization for Energy Production in Accelerator Driven Systems
M. Paraipan1,2, A. A. Baldin1,3, E.G.Baldina1,3, S. I. Tyutyunnikov1
1Joint Institute for Nuclear Research, Dubna, Russia
2Institute of Space Science, Bucharest-Magurele, Romania
3Institute for Advanced Studies "OMEGA", Dubna, Russia
XXIV International Baldin Seminar, 17-22 September 2018, Dubna
1

## Slide 2: ADS for transmutation and energy amplifier
FEAT experiment (CERN)
Total number of fission in Quinta target irradiated with deuterons (measured with SSTD)
Neutron yield from heavy metal targets
Transmutation of nuclear waste: project Omega (Japan), ATW (USA)
Concept of energy amplifier, experiments TARC and FEAT(CERN)
Project ESS (CERN)
F. Carminati, C. Geles, R. Klapisch, J. P. Revol, Ch. Roche, J. A. Rubio, C. Rubbia,An Energy Amplifier for Cleaner and Inexhaustible Nuclear Production Driven by a Particle Beam Accelerator, CERN/AT/93-47 (ET) 1993
2

## Slide 3: Energy gain for proton and ion beams
The energy gain factor G is the ratio of the produced electrical power Pprod to the power spent to accelerate the beam Pspent :
The energy deposited in the target is obtained through simulation with Geant4
We present a method for the calculation of the energy spent to accelerate a given a given ion from the data about the energetic efficiency of the accelerator for a reference beam
3

## Slide 4: M. Paraipan,A. A. Baldin, A. I. Berlev, I. V. Kudashkin, G. Mogildea, M. Mogildea, S. I. Tyutyunikov, Comparison between deuteron and carbon beams at Quinta setup, Baldin ISHEPP XXII, 2014
Comparison of Geant4 simulation with experimental data
The scheme of the target Quinta
4
Experimental and simulated distribution of fission and capture in extended U target irradiated with deuteron 2 AGeV. The data are scaled with a factor of 0.1 from a radius to another.
Total number of fission and capture in “Quinta”
Neutron yield from extended Pb and U targets irradiated with proton beams
Average neutron yield per incident proton
A. A. Baldin, A. I. Berlev, I. V. Kudashkin, G. Mogildea, M. Mogildea, M. Paraipan,S. I. Tyutyunikov, Simulation of Neutron Production in Heavy Metal Targets Using Geant4 Software, Phys. Part. Nucl. 13 2 (2016) 391-402
Fission and capture in extended U target “Quinta”

## Slide 5: The dependence of the integral energy released per projectile in quasi-infinite natU target on projectile mass number (Geant4).
5
Beams of proton, deuteron, triton, 7Li, 9Be, 11B, 12C,14N20Ne, 24Mg, 32S, and 40Ca with energies 0.3 - 10 AGeV in natural U.

## Slide 6
Method for calculation of the energy spent and the energy gain of proton and ion beams
In synchrotron :
In linac :
In cyclotron :
The relative efficiency:
G – the energy gain factor
Pprod – the electrical power produced
Pspent – the electrical power spent
ɳel – the conversion coefficient from thermal to electrical power
Edep - the energy released per incident particle
Ibeam – the beam intensity
Pbeam – the power transmitted to the particle beam
Z – the atomic number
A – the mass number
E–particle kinetic energy per nucleon
p – particle momentum
Pacc – the power spent for the functioning of the accelerator
6

## Slide 7
For a reference beam of protons with intensity I, final kinetic energy per nucleon E0 and accelerator efficiency ɳ0 we have:
In a synchrotron the energy consumption for the acceleration of a beam of particles with atomic number Z, mass number A, final energy per nucleon E, and the same beam intensity I is:
where p (p0) is the particle (reference particle) momentum per nucleon.
The relative efficiency in a synchrotron becomes:
The relative efficiency in a cyclotron is:
The relative efficiency in a linac is:
Edep and Edep0 are the energies released obtained with the analyzed particle, respective the reference particle.
7

## Slide 8
(a)
Relative (with respect to protons 1 GeV) ion efficiency as a function of beam energy for beams accelerated in a synchrotron, cyclotron, and a linear accelerator.
(c)
synchrotron
cyclotron
linear accelerator
A. A. Baldin, A. I. Berlev, M. Paraipan, and S. I. Tyutyunnikov, Optimization of Accelerated Charged Particle Beam for ADS Energy Production, Physics of Particles and Nuclei Letters, 2017, Vol. 14, No. 1, pp. 113–119
Beams of proton, deuteron, triton, 7Li, 9Be, 11B, 12C,14N20Ne, 24Mg, 32S, and 40Ca with energies 0.3 - 10 AGeV in natural U.
Energetic efficiency in natural U target
8

## Slide 9
Target with different compositions and configurations
Fuel composition: metal (alloy U, Pu, Zr, Th), carbide, MOX
Bulk target or rods with radius 0.5-1 cm, distance between 1-5 cm
Target dimensions: radius 70-90 cm, length 100-150 cm
The level of enrichment properly chosen to obtain keff 0.96-0.97
Cooling with Pb, Pb-Bi eutectic (LBE), and Na
Converter
Fuel rods
Coolant
9

## Slide 10
The energy deposited for different target configurations and different beams
10
Dimensions, cm | Material | Edep, MeV |  | 
 |  | Li-7 0.35 AGeV | Li-7 0.4AGeV | P 1.5 GeV
L120,R70,r0.5,d2 | Metal U 11% Pu239 | 9.584e4 | 1.437e5 | 1.342e5
L140,R90,r1,d5 | Metal U 14.7% U235 | 1.212e5 | 1.778e5 | 1.648e5
L150,R90, r0.5,d2 | Metal U 9.2% Pu239 | 1.031e5 | 1.567e5 | 1.536e5
L150,R90, r0.5,d2 | Carbid U 11.2% Pu239 | 9.276e4 | 1.457e5 | 1.375e5
L150,R90, r0.5,d2 | MOX 12.3% Pu239 | 1.011e5 | 1.496e5 | 1.425e5
L150,R90, r0.5,d2 | Metal Th 13.6% Pu239 | 9.423e4 | 1.429e5 | 1.381e5
L150,R90, r0.5,d2 | Metal Th 18.8% U235 | 1.015e5 | 1.518e5 | 1.572e5
L – target length
R – target radius
r – rods radius
d – distance between rods

## Slide 11
Ion | LBE | Pb | Na | Na + 20.5% U235 | Na + layer 60 cm Pb
Li7 | 1.212e5 | 1.179e5 | 2.728e4 | 1.2289e5 | 1.173e5
Proton | 2.146e5 | 2.037e5 | 5.028e4 | 2.165e5 | 2.101e5
The coolant
Metallic target 14.7 % U235, L140-R90-r1-d5, irradiated with Li 0.35 AGeV and proton 1.5 GeV.
.
The variation in actinide composition and the cooling with metals (Pb, LBE, Na) conserve the shapes of the neutron spectra and the ratio between the energies deposited by different ions.
11

## Slide 12
Converter from different materials
Core material | Core length, cm | Total neutron yield, particle-1 | Yield of neutrons with E>100 MeV, particle-1 | Deposited energy, MeV
fuel | 10 | 34.4 | 1.49 | 2.39·105
Li | 70 | 5.7 | 2.64 | 3.37·105
Be | 60 | 15.2 | 4.02 | 5.06·105
C | 51 | 8.2 | 3.25 | 3.06·105
Al | 43 | 10.2 | 2.82 | 2.78·105
Fe | 16 | 14.5 | 2.12 | 1.93·105
Neutron yield from the converter and energy released in the enriched uranium target with the converter from different materials, irradiated with 0.5 AGeV 7Li .
Target converter from very low Z materials (Li, Be, C) increases the energy released for light ions at low energy 1.4-3 times.
The effect is higher in enriched target.
. Average neutron fluence in the enriched U target without a converter U, Be, C and Fe, irradiated by the 0.5 AGeV 7Li beam.
12

## Slide 13
The choice of target dimensions
A target with higher dimensions and more compact packing ensures lower neutron leakage and the realization of the needed criticality coefficient with lower levels enrichment.
The time evolution of the Pu239 concentration for two initial levels of enrichment under irradiation with a beam of Li7, with intensity 1.25·1016.
13
U-Pu metallic target

## Slide 14
Thorium target
Metallic Th target with dimensions L150-R90-r0.5-d2 needs 13.6 % Pu239 for keff 0.96
The time evolution of the Pu239 and U233 under irradiation with a beam of Li7, with intensity 1.25·1016.
Fission cross section of neutrons in U233 and Pu239
Neutron spectrum under irradiation with Li-7
Mean fission cross section:
- 2.38 barn in U233
- 1.66 barn in Pu239
A thorium target needs a higher level of enrichment for the same geometry and a shorter period between refueling, comparing with uranium target.
14

## Slide 15
Energetic efficiency in U-Pu target
Energy gain for protons in target with converter LBE and Be
Energy gain for light ions in
target with converter LBE
Net power production for light ions in target with converter LBE
- metallic target with dimensions L150-R90-r0.5-d2
- linear accelerator (we used the data from European Spallation Source (ESS) project)
reference particle proton 2.5 GeV
the accelerator efficiency for the reference particle ɳ 0.18
the conversion coefficient from thermal to electrical power ɳel 0.4
  Ibeam 1.25·1016particles/s
15

## Slide 16
Net power production and energy gain in target with converter Be
Net power production for light ions in target with converter Be
Energy gain for light ions in
target with converter Be
16

## Slide 17
Conclusions
The energetic efficiency depends on the beam and accelerator type. The optimal energy of proton beam is 2-3 GeV in synchrotron, 1.5 GeV in linac, and 1 GeV in cyclotron. Ions starting with Li, accelerated in linac or synchrotron have a higher energetic efficiency than protons. The optimal energy for ions increases with the ion mass.
Targets with various composition, cooled with metal (Pb, LBE, Na) maintain the shape of the neutron spectrum and the ratio between the energies deposited by different ions.
Convertors from light materials (Li, Be) produce a substantial increase of the energy deposited by light ions at low kinetic energy.
It is preferable to choose a compact packing and a target with dimensions large enough in order to obtain the needed value of keff at lower levels of enrichment. We can ensure in this way higher levels of actinide burning and large periods between refueling. Light ions 7Li and 9Be with energy 0.3-0.4 AGeV realize the same energy release as a beam of proton 1.5 GeV. This allows one to obtain the same electrical power with lower energy consumption and an accelerator with ~ 2 times lower dimensions. The acceleration of 11B, and 12C at 0.7-0.75 AGeV needs an accelerator with the same dimensions as for proton beam 1.5 GeV but produces a net electrical power about 5 times higher.
The best solution from the point of view of the energy gain and miniaturization is the 7Li beam with an energy of 0.3-0.35 AGeV and a target with converter of Be and cooling with Pb or LBE.
17

## Slide 18
References
1. C. Rubbia et al., ” An Energy Amplifier for cleaner and inexhaustible nuclear energy production driven by a particle beam accelerator”. CERN/AT/93-47, November 1993
2. H. A. Abderrahim, P. Kupschua, E. Malambu, Ph. Benoit, K. Van Tichelen, B. Arien, F. Vermeersca, P. D’hondt, Y. Jongen, S. Ternier, D. Vandeplassche,” MYRRHA: A multipurpose accelerator driven system for research & development”, Nuclear Instruments and Methods in Physics Research A 463 (2001) 487–494
3. Kairat Ismailov, Masaki Saito, Hiroshi Sagara, Kenji Nishihara,” Feasibility of uranium spallation target in accelerator-driven system”, Progress in Nuclear Energy 53 (2011) 925-929
4. Pronskikh V., Mokhov N. V., Novitski I., Tyutyunikov S. I., "Energy production demonstartion for MW proton beams",12th Meeting on Shielding Aspects of Accelerators, Targets and Irradiation Facilities (SATIF-12), April 28-30, 2014, Fermi National Accelerator Laboratory, Batavia, Illinois, USA.
5. S.R. Hashemi-Nezhad , W. Westmeier, M. Zamani-Valasiadou, B. Thomauske, R. Brandt,” Optimal ion beam, target type and size for accelerator driven systems:Implications to the associated accelerator power”, Annals of Nuclear Energy 38 (2011) 1144–1155
6.Ridikas D., Mittig W., “Neutron production and energy generation by energetic projectiles:
protons or deuterons?”, Nuclear Instruments and Methods in Physics Research A 418 (1998) 449-457
7. Кошкарев Д. Г., "Оптимальные ионы для ядерного реактора с нейтронной подсветкой", Журнал технической физики 2004, том 74, вып. 7;
8. A. A. Baldin, A. I. Berlev, M. Paraipan, and S. I. Tyutyunnikov, Optimization of Accelerated Charged Particle Beam for ADS Energy Production, Physics of Particles and Nuclei Letters, 2017, Vol. 14, No. 1, pp. 113–119
18

## Slide 19
Thank you for attention !