## Slide 1: Drift Chamber detectors in the first BM@N experiment prototype Nikolay Voytishin, Vladimir Palichik LIT
Alushta, Crimea
July 11, 2015

## Slide 2: BM@N experiment
BM@N

## Slide 3: BM@N experiment
ToF-400
DC-1,2
MWPC
Dipole Magnet00
magnet
ToF-700
ZDC
DC-1,2
Detectors’ placement0

## Slide 4: Drift Chamber detector
one DC-plane schematic representation
4 double coordinate planes: wire angles 0,90,±45°, wire pitch 10 mm,
Yout ± 1.35 m, Xout ± 1.35 m, Rmin = 10 cm, 2048 wires per chamber

## Slide 5: Optimal HV value search
DC efficiency
High Voltage, (V)
Efficiency, (%)

## Slide 6
Detector resolution and alignment
330 µm
184 µm

## Slide 7
Deuteron momentum measurement
Momentum value 8.68 Gev/s with systematical error .
+2.6%
-4.3%

## Slide 8: Summary
The work is still in progress;
The Drift Chamber‘s segment builder needs further improvement and sophistication;
The Drift Cambers are one of the main detectors in the current BM@N experimental setup;
Some mistakes and uncertainties were omitted during the first runs;
The optimal HV value was chosen;
The chambers were aligned perpendicular to the beam;
The received resolution of the chamber varies for different planes, with the best value of 184 µm;
The deuteron momentum was measured as 8.68 GeV/s .
+2.6%
-4.3%

## Slide 9: Thank you for your attention!