## Slide 1: Status of the NICA project at JINR
NICA
D.Peshekhonov on behalf of the NICA team

## Slide 2
The first
Superconducting
Accelerator of
heavy
ions
1957
Synchrophasotron
1993
Nuclotron
10 GeV proton
synchrotron – leader in energy
The beginning
of high
energy physics
V.I. Veksler – author of
the phase
stability principle
A.M. Baldin
–pioneer investigation in relativistic nuclear physics
Investigation of nuclear matter at extreme densities
2019
NICA
Superconducting collider of heavy ions
From the Synchrophasotron to
the heavy ion collider
Notes: традиции: 1я базоая установка – лидер
2я – взгляд в будущее
3я – возвращение лидир.позиций

## Slide 3
Main targets of “NICA Complex”:
- study of hot and dense baryonic matter
- investigation of nucleon spin structure,
polarization phenomena
Requirements:
- development of accelerator facility providing
intensive beams of relativistic ions from p to Au
polarized protons and deuterons
with energy up to
√SNN= 11 GeV (Au79+) and =27 GeV (p)
- create modern experimental complex
NICA (Nuclotron based Ion Colider fAcility)
the flagship project in HEP of JINR
3
The project NICA was approved in 2010

## Slide 4
Study of hot and dense
baryonic matter

## Slide 5
NICA
and
the Universe

## Slide 6
Energy Range of NICA
The most intriguing and unexplored
region of the QCD phase diagram:
Highest net baryon density
Onset of deconfinement
phase transition
Strong discovery potential:
a) Critical End Point (CEP)
b) Chiral Symmetry Restoration
с) Hypothetic Quarkyonic phase
Complementary to the RHIC/BES,
CERN and FAIR experimental
programs
Comprehensive experimental program requires scan over the QCD phase
diagram by varying collision parameters: system size, beam energy and
collision centrality
NICA
Nuclotron-M
RHIC-BES
QCD phase diagram
Notes: 6

## Slide 7
coverage of max. phase space
minimum biased acceptance
free of target parasitic effects
rate is limited by detector capability
easy upgradable
fixed target
collider
advantages:
disadvantages:
rate is limited by luminosity
limited combinations “beam”/”target”
a limited phase space
momentum dependent corrections
target influenced corrections
Both, collider and fixed target approaches, are complementary and necessary for approval of potential discovery
In this view NICA and FAIR projects are complementary and both are targeting the joined efforts to discover and study new forms of baryonic matter

## Slide 8
NICA/MPD
STAR F.T.
NA-61/SHINE
HADES
CBM
SIS-100 SIS-300
STAR BES II
NICA/BM@N I
NICA/BM@N II
energy region of max.
baryonic density
Present and future HI experiments/machines
NICA/MPD will explore the whole phase space
region in the most interesting energy range
Interaction rate [Hz]
Collision energy √S [GeV]
NN

## Slide 9
Physics objectives
in spin physics

## Slide 10
Spin Physics Tasks
- Measurement of unknown or poorly known PDF’s (contributing to solution of the “spin crisis”) - MMT-DY and J/ψ production processes with transversely and longitudinally polarized p and d beams;
- Spin effects in baryon, meson and photon production;
- Spin effects in various exclusive reactions & diffractive processes;
- Spin-dependent cross sections, helicity amplitudes and double spin
asymmetries (Krish effect) in elastic reactions;
- Spectroscopy of quarkonia;
- Polarimetry

## Slide 12
Twist-2 PDFs of nucleons :
f1 - density of partons in non-polarized nucleon, (x, Q2);
g1 - helicity , longitudinal polarization of quarks in longitudinally
polarized nucleon;
h1 -- transversity, transverse polarization of quarks in transversely
polarized nucleon ;
f┴1T - Sivers, correlation between the transverse polarization of nucleon
and the transverse momentum of non-polarized quarks;
g┴1T - worm-gear-T, correlation between the transverse spin and
the longitudinal quark polarization ;
h┴ 1 - Boer-Mulders, distribution of the quark transverse momentum
in the non-polarized nucleon ;
h┴1L - worm-gear-L, correlation between the longitudinal polarization
of the nucleon (longitudinal spin) and the transverse momentum
of quarks ;
h┴1T - pretzelosity, distribution of the transverse momentum of quarks
in the transversely polarized nucleon ;
Notes: Twist-2 PDFs of nucleons

## Slide 13
Direct photons production (gluon polarization)
Direct photon productions in the non-polarized and polarized pp (pd) reactions provide information on the gluon distributions in nucleons
Vertex H corresponds to
q + qbar →γ+g or g+q→γ+q hard processes.
the polarized gluon distribution (Sivers gluon function)
can be extracted from measurement of the transverse
single spin asymmetry
Via double spin asymmetry ALL one can measure
a gluon polarization in the nucleon:

## Slide 14
experiment | CERN, COMPASS-II | FAIR, PANDA | FNAL, E-906 | RHIC, STAR | RHIC-PHENIX | NICA, SPD
mode | F.T. | F.T. | F.T. | collider | collider | collider
Beam/target | π- , p | anti-p, p | π- , p | pp | pp | pp, pd,dd
Polarization:b/t | 0; 0.8 | 0; 0 | 0; 0 | 0.5 | 0.5 | 0.7
Luminosity | 2·1033 | 2·1032 | 3.5·1035 | 5·1032 | 5·1032 | 1032
√s , GeV | 14 | 6 | 16 | 200, 500 | 200, 500 | 10-26
x1(beam) range | 0.1-0.9 | 0.1-0.6 | 0.1-0.5 | 0.03-1.0 | 0.03-1.0 | 0.1-0.8
qT, GeV | 0.5 -4.0 | 0.5 -1.5 | 0.5 -3.0 | 1.0 -10.0 | 1.0 -10.0 | 0.5 -6.0
Lepton pairs, | μ-μ+ | μ-μ+ | μ-μ+ | μ-μ+ | μ-μ+ | μ-μ+, e+e-
Data taking | 2015 | >2025 | 2013 | >2016 | >2016 | >2020
Transversity | NO | NO | NO | YES | YES | YES
Boer-Mulders | YES | YES | YES | YES | YES | YES
Sivers | YES | YES | YES | YES | YES | YES
Pretzelosity | NO | NO | NO | NO | YES | YES
Worm Gear | NO | NO | NO | NO | NO | YES
Direct γ | NO | NO | NO | YES | YES | YES
Experiments to study nucleon spin structure

## Slide 15
Scientific program - NICA White Paper
>100 contributions
Almost 200 authors from 70 centers
in 24 countries
Statistics of White Paper Contributions
France
Switzerland
Oman
Egypt
Spain
Moldova
Portugal
South Africa
Belgium
Brazil
Israel
Austria
Argentina
Slovakia
Sweden
Hungary
Japan
Indicates wide international interest
to the physics at MPD & BM@N
Notes: 15

## Slide 16
Accelerator facility
&
experimental complex

## Slide 17
Complex NICA
Experiments
with fixed targets
bld. 205
NUCLOTRON 0.6-4.5 GeV/u
IS and
LU-20 (5MeV/u)
Accelertor complex LHEP
existing
In preparation
Collider basic parameters:
√sNN = 4-11 GeV; beams: from p to Au; L~1027 cm-2 c-1 (Au), ~1032 cm-2 c-1 (p)
Collider (c=503m)
√SNN= 4 - 11 GeV
KRION-6T+HILac (3MeV/u)
Booster
(600 MeV/u)
MultiPurpose
Detector
SPD
MPD
BM@N
Notes: Комплекс свехпроводящих ускорителей NICA и экспериментальных установок представлен на этом слайде.
Синим показаны существующие объекты:
линак на 20 МэВ,
Нуклотрон
Зона для экспериментов с фиксированными мишенями на выведенных из нуклотрона пучках.
Красным – то, что Предстоит построить и запустить:
новый линак для тяжелых ионов;
бустер – промежуточный этап ускорения для достижения большей интенсивности;
коллайдер с периметром около 500 м;
установку BM@N для экспериментов с фиксированной мишенью;
установку MPD на первом пересечении пучков коллайдера и
установку SPD на втором пересечении .
Коллайдер рассчитан на диапазон энергий от 4 до 11 ГэВ для ускорения золота с рекордной для тяжелых ионов светимостиью 1027 см-2 с-1.

## Slide 19
January’2015:20 test piles
Additional 50 m drilling for soil analysisfor special vibration tests
Territory preparation
completed ~60 000 m2
The machine pressing the test piles
Contract for preparatory works (planning of the territory, network removal, water-lowing, roads, pile-field planning, etc) – signed in March 2015

## Slide 20
Civil Construction of NICA Complex
18 September 2015 JINR and STRABAG signed a contract for General construction works for the NICA complex: 43 months period
Notes: Основные этапы создания комплекса NICA
в 2010 году утвержден проект NICA и завершен I этап модернизации Нуклотрона, начаты работы по ускорительному комплексу и многоцелевому детектору MPD (MultiPurpose Detector) , которые завершатся в 2019.
С 2012 года готовится эксперимент с фиксированной мишенью - детектор BM@N (I этап),первые результаты с которого ожидаются в 2017
- Идет подготовка проекта Spin Physics Detector (SPD)

## Slide 21
Civil Construction of NICA Complex
The whole Complex is split into several Objects:
MPD Hall 2017
West semi-ring 2017
Beam transfer channel 2018
SPD Hall 2019
East semi-ring 2019
Beam extraction
Reconstruction of building #1 affect Nuclotron operation
should be taken into account :
Nuclotron operation plans
MPD magnet fabrication schedule
Equipment installation plans
Notes: Основные этапы создания комплекса NICA
в 2010 году утвержден проект NICA и завершен I этап модернизации Нуклотрона, начаты работы по ускорительному комплексу и многоцелевому детектору MPD (MultiPurpose Detector) , которые завершатся в 2019.
С 2012 года готовится эксперимент с фиксированной мишенью - детектор BM@N (I этап),первые результаты с которого ожидаются в 2017
- Идет подготовка проекта Spin Physics Detector (SPD)

## Slide 22
Area for magnet assembly & tests
Cryogenics
Workshop for microstrip detector assembly & tests
Workshop for RPC assembly & tests
Workshop for TPC assembly & tests
NICA Infrastructure
Notes: Основные этапы создания комплекса NICA
в 2010 году утвержден проект NICA и завершен I этап модернизации Нуклотрона, начаты работы по ускорительному комплексу и многоцелевому детектору MPD (MultiPurpose Detector) , которые завершатся в 2019.
С 2012 года готовится эксперимент с фиксированной мишенью - детектор BM@N (I этап),первые результаты с которого ожидаются в 2017
- Идет подготовка проекта Spin Physics Detector (SPD)

## Slide 23
2013
June 2015
SC Magnets for Booster, Collider & SIS-100/FAIR
workshop at VBLHEP JINR (bld. 217)

## Slide 24
LHe Liquefier OG-1000
(installation & commissioning): 96% completed
(2010-2015)
Reconstruction of bld. 32:
14% completed
(2014-2015)
Helium satellite refrigerator of Booster and Collider:
5% completed
(2016-2017)
Two He screw
compressors
(delivered):
94% completed
(2011-2015)
LN2 Re-condensation
(liquefier + 2 compressors)
12% completed
(2012-2018)
LHe 40m3 reservoir:
0% completed
(will start in 2016)
Gaseous He purification system:
0% completed
(will start in 2016)
He satellite refrigerator for Booster & Collider:
5% completed
(2014-2018)
Development of the NICA Cryogenics
The cooling power
should be doubled
from 4 kW to 8 kW @ 4.5K

## Slide 25
CERN & JINR signed MoU for Collaboration in manufacturing of the carbon fiber spaceframes for the (SiTS) for BM@N & MPD at NICA & CBM at FAIR
Workshop for microstrip detector assembly & tests
clean room for Silicon Vertex
Detector assembly is ready;
the workshop
will start operation in 2015.
Project status:
in accordance with plans
CBM-MPD Consortium

## Slide 26
Workshop for assembly & tests of the TOF detectors
- the detector assembly (mass production) will start in Febr. 2017
- will be fully completed in December 2018
bench for ultrasonic cleaning of glass,
detector assembly bench
supermodule assembly & test bench
glass drying bench
in operation
in operation
in operation
in preparation

## Slide 27
Workshop for TPC assembly & tests
(in preparation)

## Slide 28
Injector (ion sources, linacs)
booster
collider
Accelerator status
Notes: Основные этапы создания комплекса NICA
в 2010 году утвержден проект NICA и завершен I этап модернизации Нуклотрона, начаты работы по ускорительному комплексу и многоцелевому детектору MPD (MultiPurpose Detector) , которые завершатся в 2019.
С 2012 года готовится эксперимент с фиксированной мишенью - детектор BM@N (I этап),первые результаты с которого ожидаются в 2017
- Идет подготовка проекта Spin Physics Detector (SPD)

## Slide 29: Progress in NICA injection complex: ion sources Source of polarized particles (SPP)
5.4T magnetic field reached in a robust regime. Test gold ion beams have been produced:
Au30+ ÷ Au32+, 6 x108 ions/pulse,
20 ms ionization time
Au51+÷ Au54+ , 1.3x108 ions/pulse
SPP is now commissioned to provide
1010 polarized deuterons/pulse
29
The achieved electron string current density J ~1400 A/cm2
fits to the NICA-MPD requirements
Heavy ion source: Krion-6T ESIS @ LU-20
Electron String Ion Source

## Slide 30
RFQ resonator:
copper plating finished. Delivered to ITEP for commissioning in 2015
RFQ resonator. Production started in 2013 (ITEP, MEPHI, VNIITP Snezhinsk)
NICA Heavy ion injector
High current (10 mA) HI Linac (HILAC) “BEVATECH OHG” in Offenbach/Mainz
NICA light ion injector (LU-20)
RFQ section in new HILAC hall
HILAC delivered to Dubna, start of commissioning in July 2015
Notes: HILAC: Radio Frequency Quadrupole + Medium Energy Beam Transport + two Interdigital H-type Drift Tubes

## Slide 31
The Booster - commissioning in 2017
40 Dipole SC magnets
ultra high vacuum - electron cooling
48 Quadruple SC magnets

## Slide 32
Injection
from HILac
Extraction
to Nuclotron
Satellite refrigerator,
Measurement period,
Energy evacuation
Electron cooling
RF
HILac
LU20
Booster synchrotron
inside Synchrophasotron yoke, 3-660 MeV/u

## Slide 33
Sextupole corrector prototype for booster and SIS100 at assembly
Booster dipole (up) and quadrupole lense and Q-doublet (down)
Collider dipole (up) and quadrupole lense (down)
Booster UHV beam chamber (curved)
Full-scale Nuclotron–type superconducting prototypes of dipole and quadrupole magnets for the NICA booster and collider were manufactured at LHEP JINR, have successfully passed the cryogenic test on the bench. Serial production of the magnets: for the booster started in Dec. 2014
for the collider will start in Jan. 2016

## Slide 34
 |  | 2015 |  |  |  | 2016 |  |  |  | 2017 |  |  |  | 2018 |  |  |  | 2019 |  |  |  | 2020 |  |  | 
 |  | I | II | III | IV | I | II | III | IV | I | II | III | IV | I | II | III | IV | I | II | III | IV | I | II | III | IV
Booster |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
dipoles | 40+3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
quadrupoles | 48+6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
multipole correctors | 40+4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Collider |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
dipoles | 80+5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
quadrupoles | 86+5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
multipole correctors |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
nonstructurals |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SIS-100 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
pre-series quadrupole | 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
pre-series sextupole correctors | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
pre-series dipole correctors | 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
pre-series multipole correctors | 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
quadrupole | 166 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sextupole correctors | 48 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
dipole correctors | 83 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
multipole correctors | 12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Magnets (booster+ collider+SIS-100) production plan
Booster magnets in 2015:
16 dipoles
24 quadrupoles

## Slide 35
MultiPurpose Detector (MPD)
Baryonic Matter at Nuclotron (BM@N)
the fixed target experiment
at the Nuclotron
at the Collider
SPD (Spin Physics Detector) start of Stage I - 2023
project is under preparation
NICA detectors
start of Stage I - 2017
start of Stage I - 2019

## Slide 36
BM@N (2017): Study of dense baryonic matter
at < 6 GeV/u (fixed target mode)
Physics is complementary to the MPD (2019) program
& will be up-to-date even after MPD start-up
BM@N 1st stage program:
- study of yields of hadrons, hyperons, and light nuclei, 2017-2019.
BM@N program with heavy ion high-intensity beams:
- study of the elliptic and directed flows, production of hyperons with S=2
and hyper-nuclei

## Slide 37
Parameter | Project (2017) | 
Magnetic field, T | 2.0 (B = 42.8 Tm) | 
Field ramp, T/s | 1.0 | 
Repetition period, s | 5.0 | 
 | Energy, GeV/u | Ions/ cycle
Light ions  d | 7.0 | 51010
Heavy ions | With KRION-6T & Booster | 
40Ar18+ | 5.9 | 21010
56Fe26+ | 6.4 | 11010
124Xe48/42+ | 5.0 | 2109
197Au79+ | 5.5 | 2109
Polarized beams | With SPI | 
p | 12.9 | 11010 *)
d | 6.6 | 11010
*) With the Siberian snake
Nuclotron Beams

## Slide 38
BM@N: the 1st stage approved in 2012
Collaboration of 19 scientific centers:
INR, SINP MSU, IHEP + S-Ptr Univ. (RF);
GSI, Frankfurt U., Gissen U. (Germany):
+ CBM-MPD IT-Consortium, …
area prepared for detector installation
Physics:
hyperon & hypernuclei production
hadron femtoscopy
in-medium effects for strange
& vector mesons
electromagnetic probes (optional)
BM@N schematic view

## Slide 39
BM@N technical run in February-March 2015
ToF400
ToF700
DCH
ZDC
d, C12 beams, T0= 3.5– 4.2 GeV
analyzing magnet
SP-41
MWPC
T0T
target C12
BM
Tasks for test run:
trace d, C12; beam profile/structure
test detector response: ToF400/700 (part),
DCH-1,2 (part), ZDC (part),T0T, BM
test integrated DAQ / trigger based on
T0T in magnet
MWPC
ZDC
on movable
platform

## Slide 40: NICA collider mode MPD & SPD

## Slide 41
9 m length, 6 m in diameter
Magnet: 0.66 T
superconducting solenoid
Tracking: TPC, IT, ECT
ParticleID: TOF, ECAL, TPC
T0, Triggering: FFD
Centrality, Event plane: ZDC
MPD potential advantages:
Hermetic & homogenous acceptance (2in azimuth), low material budget
Good tracking performance and powerful PID (nuclei, hadrons, e, )
High event rate capability and reliable event separation
FFD
MultiPurpose Detector (MPD)
Stage 1: TPC, barrel (TOF, ECAL), ZDC, FFD
Stage 2: Endcaps (tracker, TOF, ECAL) + IT

## Slide 42
MPD status
Magnet – survey for producers
Integration – project preparation
TOF, ECAL, ZDC – TDR are ready
FFD – fabrication stage
TPC
  assembly area preparations
  fabrication of basic elements
  readout chambers – production + R&D (alternative)
  FEE (ALTRO-based FE card prototype - preproduction stage
MPD first stage program:
- studying the properties of the hot and dense baryonic matter in the central rapidity range;
- search for phase transitions (observables – particle yields and spectra) including partial restoration of chiral symmetry (observables – yields of di- leptons);
- search for the critical end-point (observables – event by event fluctuations, particle correlations)

## Slide 43
SPD status
LoI-02.06.14 (17 institutions):
SPIN PHYSICS EXPERIMENTS AT NICA-SPD
WITH POLARIZED PROTON AND DEUTERON BEAMS
18.02.2015 JINR SPD working group formed:
- to start the work on SPD TDR
- to organize the work related to the acceleration of
polarized particles and beam polarization measurements
- to organize formation of the international collaboration

## Slide 44
NICA schedule
  The decommissioning is foreseen after 2045

## Slide 45
NICA Collaboration
ARE

## Slide 46
NICA as one of the 6 mega-science projects in RF
08 Aug’13: Representatives of 13 countries, 6 signed
to join the mega-science project NICA
08 Aug’13: Representatives of 13 countries, 6 signed to join (Belarus, Bulgaria, Germany, Kazakhstan, RF, Ukraine). China and South Africa – are ready to join.
The Parties have agreed to inform their Governments about the Meeting on Prospects for Collaboration in the Mega-Science Project “NICA Complex” and to express their interest in preparing corresponding multilateral Agreement and in taking steps for approval by their countries
Germany (BMBF, GSI) – to the Test Facility for SC magnets and Si tracker Lab; MoU
China (ASIPP) – to the HTSC current leads, SC magnets, vacuum systems; MoU
USA (FNAL) – to the NICA collider stochastic and electron cooling systems; MoU
CERN – to the BM@N and MPD elements (drift chambers, MM systems…); MoU
Rep. of South Africa – cryostats, diagnostics for SC ion source, cryogenics. MoU

## Slide 47
exchange of know-how on designing and constructing detector and accelerator components
involvement in common activities to bundle resources and create additional synergies
providing support in coordination, reviewing and training
CREMLIN objectives for
NICA & FAIR:
NICA & FAIR became the part (Work Package 3) of CREMLIN project (Connecting Russian & European Measures for Large-scale Research Infrastructures) in the framework of HORIZON 2020
Signed by 19 European Institutes (including JINR + 5 Russian Institutes)
Project kick-off:
Moscow, Oct. 5-8, 2015
Extension of the International Cooperation
Bulgarian authorities (Nuclear Regulatory Agency, as a representative in JINR CPP and Ministry of Education) take a decision about submission of the NICA project to ESFRI Roadmap. Special letter of Commitment prepared and Letter of support for the submission of the NICA project.
Authorities of Czech Republic, Romania and Slovakia kindly considered favorably the support to this submission.
The ESFRI Roadmap identifies new Research Infrastructures (RI) of pan-European interest corresponding to the long term needs of the European research communities, covering all scientific areas, regardless of possible location.
Project descriptions highlight the manner in which they would impact on science and technology development at international level, how they would support new ways of doing science in Europe, and how they would contribute to the enhancement of the European Research Area.

## Slide 48
Concluding remarks
the civil construction of NICA complex started
the magnet assembly workshop is in operation, the series SC magnets production started
MPD sub-detectors are close to the stage of fabrication
SPD LoI prepared and SPD working group formed
International cooperation around NICA is growing

## Slide 49
Thank you!
NICA
FAIR
HL LHC
Science brings nations together !

## Slide 51
Ring circumference, m | 503.04
heavy ions | 
b, m | 0.35
energy range for Au79+: √SNN, GeV | 4 - 11
r.m.s. Dp/p, 10-3 | 1.6
peak Luminosity for Au79+, cm-2 s-1 | 1x1027
polarized particles | 
max. energy for polarized p, Gev | 27
peak Luminosity for p, cm-2 s-1 | 1x1032
NICA collider major parameters

## Slide 52
cost of the full-scale NICA project is estimated as $530M;
the Russian Federation, as the host country,
has committed itself to invest $250M in the project.
the rest $50M have been already contributed
and expected from Germany, CERN, USA, China, RSA
and other countries - participants of the NICA project
on the basis of bilateral agreements
the breakdown of contributions to the major parts of the NICA Complex are as the following:
the first guaranteed contribution to the accelerator
and detectors (BM@N, MPD and SPD) construction - $230M is committed by the JINR;

## Slide 53
For the running phase of the NICA complex
it is expected an additional contribution
at the level of ~ 100 M$
from EU partners interested in
the development of extracted beams
and constructions of detectors for basic
and applied researches.
Bulgaria, Romania, Slovakia, Czech Republic
the Poland will definitely participate in several
experiments at NICA in basic and applied researches
contributing by dedicated grants.

## Slide 54
The operational costs for the NICA accelerator complex
per year could be split on
the provision of required consumables and power,
which are estimated as $5M
for gases and other consumables
and ~ $4M for electricity and water;
the maintenance of the facility,
which is evaluated at the level of $11M.
All of these expenses are evaluated in the prices of 2015
taking into account a present salary of the personal.
The operational costs for run of experiments
will be covered by collaborations
in accordance with the corresponding MoU’s

## Slide 55
We plan to extend existing e-infrastructure of the JINR
used in the LHC experiments in frames
of the Worldwide LHC Computing Grid (WLCG) project (grid Tier-1 for CMS, Tier-2 for ATLAS, Alice, CMS, LHCb), cloud infrastructure and hybrid HPC cluster up to necessary power for MPD and BM@N data flow processing and storage.
It is expected about 10 PB data / year starting from 2020.
A distributed e-infrastructure inside JINR was organized
as 2 off-line Tier-0 and Tier-1 computer centers.
The simulation concept for
grid-cloud services of contemporary HENP experiments
of the Big Data scale was formulated
in practicing the simulation system developed at JINR.

## Slide 56
The simulation of some processes of the NICA-MPD-SPD
Tier0-Tier1 distributed computing is considered
as an example of this approach applications.
The e-IRG guidelines “Best Practices for the use
of e-Infrastructures by large-scale research infrastructures” are used for RI planning and construction.
It should be also noted
that EGI High Throughput Computing Solution
are available for as at international and national levels.
EGI's solutions also include data infrastructure services,
mainly grid storage, cloud storage, file transfer service
and file metadata catalogue.

## Slide 57
The current situation is as following:
10 Gb/s local network;
20 Gb/s external channel;
connections with different scientific networks
- LHCOPN
- LHCONE
- GEANT.
To meet NICA requirements, the performance
of existing internal and external channels
will be upgraded
up to 100 Gb/s.

## Slide 58
Data analysis tool for the NICA experiments
is developed by MPD software group on the basis
of the ROOT framework (CERN)
and FAIRroot packages (GSI, Germany).
This framework was developed together with
the software group from the CBM/FAIR experiment.
It is updated regularly with including the local changes
in the code and when external packages like GEANT
or ROOT are needed to be updated.
This framework is tested by the users
from the local experiments (MPD, BM@N)
and from the CBM experiment as well.

## Slide 59
Synchrocyclotron 680 MeV (1949)
Synchrophasotron 10 GeV (1957)
V.Veksler
M.Meshcheryakov
Accelerators with record parameters built up at JINR