## Slide 1
UPGRADE OF THE GERDA EXPERIMENT
N. Rumyantseva

## Slide 2
Searching for 0 helps to understand:
Nature of  (Dirac or Majorana)
Neutrino mass scale
Neutrino hierarchy
Neutrinoless double beta decay
Isotope |  |  | Nat. ab. (%)
48Ca | 6.3 | 4273.7 | 0.187
76Ge | 0.63 | 2039.1 | 7.8
82Se | 2.7 | 2995.5 | 9.2
100Mo | 4.4 | 3035.0 | 9.6
130Te | 4.1 | 2530.3 | 34.5
136Xe | 4.3 | 2461.9 | 8.9
150Nd | 19.2 | 3367.3 | 5.6
Isotope |  |  | Nat. ab. (%)
48Ca | 6.3 | 4273.7 | 0.187
76Ge | 0.63 | 2039.1 | 7.8
82Se | 2.7 | 2995.5 | 9.2
100Mo | 4.4 | 3035.0 | 9.6
130Te | 4.1 | 2530.3 | 34.5
136Xe | 4.3 | 2461.9 | 8.9
150Nd | 19.2 | 3367.3 | 5.6
Target mass and detector efficiency as high as possible
“Zero-background” to have linear increase of sensitivity vs exposure
Experimental sensitivity:
Zero background:
Non-zero background:
exposure (kg yr)
energy resolution (keV)
background index (counts/keV kg yr)
Notes: Neutrinoless double beta decay is a hypothetical lepton number violating process, where two neutrons convert into two protons and two electrons. If we observe this process, it would mean that the neutrino
is its own anti-particle (Majorana particle). It will provide access to the absolute mass scale of neutrinos, and support extensions of the Standard Model.
There are 35 isotopes for which the double beta decay (both 2 neutrino and neutrinoless) is energetically allowed, however its probability strongly depends on the decay energy. So only a few isotopes with the decay energies more than 2 MeV are under consideration now.
The sensitivity of 0νββ search is proportional to the exposure. That is why any 0νββ experiment should use pretty big mass of isotope and keep the efficiency as high as possible. Another critical point is a
background in the region of interest, since only in the case of “zero” background, sensitivity is linearly increase with exposure.

## Slide 3
The GERDA experiment is an ultra-low background experiment aimed to search for 0 decay of 76Ge.
Ge detector
76Ge  76Se + 2e- + 2νe
Q = 2039 keV
● 76Ge → 76Se + 2e- with Qββ = 2039 keV
● Source and detector are the same
→ high detection efficiency
● Isotope enrichment up to 88% for
detector material
● Intrinsically pure material
→ low background
● Excellent energy resolution
→ 2νββ background suppressed
● High density material → ββ point-like
→ backgrounds can be discriminated and rejected
Neutrinoless double beta decay search with 76Ge
Notes: In the GERDA (GERmanium Detector Array) experiment, bare germanium detectors are operated in liquid argon (LAr). The detectors are made from germanium with the fraction of the 76Ge isotope enriched to about 88%. Since the source and the detector of 0νββ decay are identical (in this calorimetric approach), the detection efficiency is high.
Germanium detector is a pure material – so it helps to reach very low background level.
The experimental signature of 0νββ decay is a sharp peak at the end of continuous 2νββ spectrum – so the energy resolution is essential. This gives a serious advantage to Ge projects thanks to the excellent energy resolution of semiconductor detectors.

## Slide 4
Features:
Low-A shield, no Pb
Bare Ge-diodes array in liquid argon (LAr)
LAr is used as veto system
Good pulse shape discrimination capability of Ge detectors
GERDA will collect data until the end of 2019
GERDA Phase II: design
3500 m.w.e
1.25 µ / (m2 h)
Notes: The GERDA experiment is located at the Laboratori Nazionali del Gran Sasso in Italy. A rock overburden of about 3,500 m water equivalent removes the hadronic components of cosmic ray showers and reduces the muon flux to 1.25 muons m−2 h−1.
GERDA uses enriched germanium detectors arranged in strings within a cryostat filled with liquid argon. The liquid argon acts both as cooling and active shielding medium. The cryostat is enclosed by a large tank with ultra-pure water with PMTs. These PMTs detect Cherenkov light from muons passing through the setup. A clean room on top of the cryostat and water tank houses a glove box and the lock for assembling of Ge detectors.
Close to the detector array we have LAr veto system, which allows to readout the scintillation light from Ar and, thus, to additionally reduce the background.
Another important feature of the GERDA is a possibility to reach better background index by pulse shape discrimination in Ge detectors.

## Slide 5
GERDA collaboration
GERDA members from JINR:
V. Brudanin, D. Borowicz, V. Egorov, M. Fomina, K. Gusev, A. Klimenko, O. Kochetov, A. Lubashevskiy, I. Nemchenok, S.Nepochatich, N. Rumyantseva, V. Sandukovsky, E. Shevchik, M. Shirchenko, A. Smolnikov, I. Zhitnikov, D. Zinatulina (Total FTE = 7.5)
Notes: The GERDA collaboration includes ~ 110 members from 16 institutions and 6 countries. The JINR group in GERDA consists of 17 people and plays important role in all parts of the experiment: operations with germanium detectors, production and integration of active veto systems (that is plastic muon veto, liquid argon veto, nylon mini-shrouds) and data analysis.

## Slide 6
60 kg yr of data collected in Phase II by April 2018
82.4 kg yr in total (Phase I + II)
Unique background indices achieved:
  Coax: cts/(keV∙kg∙yr)
  BEGe: cts/(keV∙kg∙yr)
New 2018 limits:
  Median sensitivity for limit setting:
    (world best!)
  Best fit → no signal
  Probability to have stronger limit 63%
after all cuts
best in the field when normalized to FWHM!
Preliminary
GERDA reached important milestone for 0νββ search!
GERDA: results 2018
Notes: GERDA Phase II is taking data since December 2015. 60 kg yr of data were collected in Phase II by April 2018. Together with Phase I we have more than 80 kg yr. The background index is improved by almost two times compared to the previous release and stays the best among all double beta decay experiments.
The unprecedented median sensitivity of more than 1026 yr was reached first time ever. This is very important milestone for 0νββ search.

## Slide 7
Upgrade of the GERDA experiment aimed to:
  Test the novel detectors + increase the mass of 76Ge
    Total increase of 76Ge mass ~ 6 kg!
  Show the possibility to improve the background index
    Exchange all cables by new ones with better radiopurity
    Replace old LAr veto by improved version
  Repair broken JFETs and electronic channels
  Prove the robustness and reproducibility of the GERDA approach (very important for the next generation Ge project)
GERDA: upgrade 2018
Notes: In 2018 the GERDA collaboration performed the upgrade aimed to test the novel Ge detectors and increase the mass of 76Ge.
Another goal was to show the possibility to improve the background index and to prove the robustness and reproducibility of the GERDA approach, which is very important for the future Ge experiments.

## Slide 8
New LAr veto:
  new fiber curtain (improved light collection) + central module to read out hidden Ar volume
810 fiber ends, 90 SiPMs
1215 fiber ends, 135 SiPMs
Old curtain
New curtain
Central module
New readout
9 SiPMs mounted on fused
synthetic quartz substrate
Designed
Produced
Installed
228Th spectra before and after upgrade
GERDA: successful upgrade 2018
Designed, produced and installed by common TUM & JINR team
Notes: The new liquid argon veto system includes new fiber shroud with improved light collection and central module needed to view hidden LAr volume.
The new liquid argon veto system has been produced, tested and installed in GERDA by common TUM and JINR group.

## Slide 9
All detectors were dismounted from the strings and holders, bonded with new cables and mounted back
Broken electronic channels repaired and protective diodes installed
New signal cable routing to reduce the cross-talk and improve resolution
GERDA: successful upgrade 2018
 | Pyralux 3 mil TECNOMEC | Cuflon HV Haefele | Cuflon signal Haefele
226Ra | < 3.8 mBq/kg x 0.5 g → < 2 μBq | (8 ± 2) mBq/kg x 2.7 g → (22 ± 5) μBq | (50 ± 10) mBq/kg x 0.5 g → (25 ± 5) μBq
228Th | < 5.5 mBq/kg x 0.5 g → < 3 μBq | < 8.3 mBq/kg x 2.7 g → < 22 μBq | < 21 mBq/kg x 0.5 g → < 11 μBq
40K | (0.11 ± 0.03) Bq/kg x 0.5 g → (55 ± 15) μBq | (0.11 ± 0.03) Bq/kg x 2.7 g → (300 ± 80) μBq | (0.2 ± 0.1) mBq/kg x 0.5 g → (100 ± 50) μBq
60Co | < 0.77 mBq/kg x 0.5 g → < 0.4 μBq | < 2.3 mBq/kg x 2.7 g → < 6.2 μBq | < 17 mBq/kg x 0.5 g → < 8.5 μBq
237Cs | < 1.2 mBq/kg x 0.5 g → < 0.6 μBq | < 2.4 mBq/kg x 2.7 g → < 6.5 μBq | < 10 mBq/kg x 0.5 g → < 5.0 μBq
New cables
after upgrade
before upgrade
Old cables
Notes: All detector cables were exchanged by new ones with better radiopurity. To do this we had to dismount all 40 detectors from strings and holders, rebond them with new cables and mount everything back.
We have also repaired all broken electronic channels. In addition, the routine of signal cables has been changed. That helped to improve the energy resolutions for most of detectors.

## Slide 10
GERDA: successful upgrade 2018
5 inverted coaxial detectors made from 76Ge have been produced, characterized and mounted in the GERDA setup to replace the detectors made from natural Ge
Entire upgrade operation lasted ~5 weeks in April/May + 1 week in July
  Performed by JINR + MPIK + TUM + INFN team
All electronic channels are functioning
No deterioration of detectors leakage current after upgrade
New fiber shroud and central fiber module are working
Energy resolutions improved
Novel 76Ge detectors installed
Results of upgrade 2018:
Only enriched detectors in GERDA now!
GERDA will collect data until the end of 2019 then…
Notes: 5 novel inverted coaxial detectors, which are good candidates for tonne-scale Ge project, were produced, characterized and installed. 76Ge mass is increased by about 6 kg!
The upgrade operation was successfully performed in Spring and Summer 2018. It took less than 2 months (note, that all detectors had to be fully disassembled and assembled again). It performed with the leading role of JINR specialists and brought the very useful experience for the next generation germanium project LEGEND.

## Slide 11
Large Enriched Germanium Experiment for Neutrinoless ββ Decay
First stage (L200):
(up to) 200 kg in modified GERDA infrastructure at LNGS
bkg reduction by factor 3-5 w.r.t GERDA
Sensitivity 1027 yr
Plan to start data taking in 2021
Subsequent stages:
1000 kg (staged)
timeline connected to DOE down select process
bkg factor 30 w.r.t GERDA
Location tbd
Sensitivity 1028 yr
LEGEND: the best from GERDA and MJD
Notes: The GERDA will take data until the exposure of 100 kg yr will be reached (at the end of 2019). At that time the sensitivity should be well above 1026 yr. However, this sensitivity will not allow getting an information about neutrino mass hierarchy.
To answer this question the new generation experiment LEGEND is being built. It is foreseen at least two phases of the project. The first phase (LEGEND-200) will operate with ~ 200 kg of enriched isotope and the expected sensitivity will be 1027 years. The second phase (LEGEND-1000) will use 1000 kg and would be reach 1028 years.
It should be noted, that a germanium experiment has good discovery potential of because the excellent energy resolution of Ge detectors. LEGEND-200 will be carried out in the modified GERDA infrastructure at LNGS. The goal is to start data taking in the first phase of LEGEND in 2021.

## Slide 12
Thank you for attention

## Slide 14
Pulse Shape Discrimination for BEGe detector

## Slide 15
Background reduction concept
Source: AJ Zsigmond’s talk at Neutrino 2018

## Slide 16
T1/2 limit (90% C.L.)
GERDA-II / MJD
LEGEND 200kg
LEGEND 1000kg
18 meV, different NME
GERDA-II / MJD
LEGEND 200kg
LEGEND 1000kg
Discovery (50% chance for a 3σ signal)
N.B.: background-free operation
is a prerequisite for a discovery
T1/2 unknown, BSM → 'around corner‘
background reduction in steps → phased approach
inputs: 60% efficiency (GERDA number)
Background: GERDA/MJD ~ 3 cts/(FWHM t yr)
200 kg ~ 0.6 cts/(FWHM t yr)
1000 kg ~ 0.1 cts/(FWHM t yr)
LEGEND: sensitivity

## Slide 17
= phase space factor
= nuclear matrix element
= electron mass