## Slide 1
ELECTRONICS OF THE FISSION FRAGMENTS SPECTROMETER "COMETA-F"
Oleg Strekalovsky1,3, Dmitry Kamanin1, Yury Pyatkov1,2, Alexandr Strekalovsky1 Vladimir Juchko1
1Joint Institute for Nuclear Research
2National Nuclear Research University “MEPHI”
3 University “Dubna”
Notes: At present, we cannot say that we understand the nuclear fission process

## Slide 2
FOBOS
mini-FOBOS
FLNR / Sector №5: dynamics of heavy nuclei interaction, fission of heavy and superheavy nuclei / Group №1: of fission of weakly excited nuclei
>1990y
Rare processes: multibody decays and their “fine structures”.
Eur. Phys. J. A 45, 29-37 (2010)
Notes: In our group of the Flerov LNR we study nuclear decay. At first at Fobos spectrometer installed on U400 accelerator
Then at minifobos two arms spectrometer with neutron belt and now
at the Pin diods spectrometer
One unusual effect was found at fobos experiments, which was called collinear cluster tri-partition (three-particle,?) decay

## Slide 3
D.V. Kamanin, Yu. V. Pyatkov
"Clusters in Nuclei - Vol.3"
ed. by C. Beck,
Lecture Notes in Physics 875,
pp. 183-246 (2013)
Summary of the previous results on CCT
Notes: certainly, the results were published in European physical journal

## Slide 4
Angular dependence of the break-up yield
At the large angles of scattering of the knocked–out ions from the foil
conventional elastic Rutherford
scattering takes place.
Notes: At first effect was found using ordinary for millenium analogue electronic and set of coordinate-sensitive avalanche counters, Bragg ionization cameras, phosvich detectors. Now we used absolutey different digital electronics, detectors and saw the same effect.
Two arme spectrometer Cometa consist of start detector and a few matrix of PIN diodes

## Slide 5
18x18mm
Notes: Start signal for time interval measurement is taken from start detector, which consists of Au foil and shevron of two multi channel plates. Pin diode is used for simultaneous energy
and stop-time of ion registration. We used home made fast transistor amplifiers, placed very close to detector and which worked in vacuum.

## Slide 6: SWITCH CAPACITY ARRAY DT5742, V1742
DT5742
V1742
DRS4
PLL-regulated
Sampling Speed
Notes: In the three-particle fission model, two fragments are expected to move in one direction and one fragment in the opposite. The flight time is tens of ns. We need a registration system with good energy and time resolution. The registration of the waveform eliminates pile-ups and noise and allows the use of different mathematical methods for analysis.
Fast ADCs with more than 12 bits are expensive
The solution was the use of multi-channel recorders based on the DRS4 chip

## Slide 7
Notes: 7
chip was developed at the Paul Scherrer institute. Switch capacity array consists of 1024 capacitors.

## Slide 8
SONET-2
Notes: A fiber optic network is used for the connection to the PC.

## Slide 9
Notes: Each of registered events looks like this one.

## Slide 10
Notes: if the correction procedure is applied to the ramp voltage recorded in the recorder memory (on the left), then the obtained values will have the following form (on the right).
Data correction procedure takes a lot of time, and now we do it offline.

## Slide 11: Измерения временных интервалов несколькими регистраторами
Схема подключения временного калибратора ORTEC 462 к оцифраторам DT5742
Распределение временных интервалов при подаче сигнала Старт на вход одного
регистратора, а сигнала Стоп на вход другого
регистратора
Распределение времени, полученное при измерении временных интервалов от калибратора при подаче сигналов на входы разных микросхем DRS4 после учета поправки положения сигналов в соответствии с положением соответствующих триггерных сигналов
Notes: The ortec time calibrator generates test signals with a duration increasing by 10 ns for each next pulse.
The time distribution for one dc4 circuit looks like this. If the start signal is taken from one circuit, and the stop comes to another, then the resolution becomes very poor. But if we take into account the time shift between the recorded trigger signals, then this correction allow adequately restore the correct distribution.

## Slide 12
Разрешение = Tsample/12 Tsample = 200 пс
Интерполяция позволяет улучшить временное разрешение
Зависимость от времени нарастания и амплитуды импульса
CFD, LED, другие привязки?
Notes: when measuring time, the blue line is the real signal. The error of the moment of determining the zero line intersection is associated with an error due to the ADC bit depth and the interpolation error

## Slide 14
Notes: when restoring the mass of fragments, we use the well-known distribution of spontaneous fission of Cf. This allows one to take into account the effect of pulse height deficit and plasma delay.

## Slide 15: HI mass reconstruction at different energies
Time-of-flight mass-spectrometry of heavy ions in a wide range of masses and energies using PIN diodes.
Kamanin D.V.1, Pyatkov Yu.V.2,1, Zhuchko V.E.1 , Strekalovsky A.O.1 , Strekalovsky O.V.1, S. Heinz 3, Ilić S. 4,1 , Alexandrov A.A.1, Alexandrova I.A.1, Jacobs N.5, Kuznetsova E.A.1, Malaza V5. (submitted to NIM A in November 2015)
Experimental setup
at IC-100 beam line
The developed mass recovery procedure allows determining mass in a wide range of masses and energies (ions from 12С to 132Хе in the energy range ~ (10-100) MeV).
Notes: the correctness of the reconstruction method was verified experimentally at the cyclotron in FLNR.

## Slide 16
COMETA - F

## Slide 17
Notes: The basis of the data collection system are 32-channel digitizers. The B895 discriminators, together with the trigger unit, allow you to generate a data acquisition trigger. The data recorded in the buffer over the fiber-optic network is transmitted to a PC and then to 120 TB of the SInology storage.

## Slide 18: Установка Комета
Общий вид спектрометра Комета
Notes: all spectrometer electronics installed in one VME crate

## Slide 19
Notes: software for data collection system developed in LV environment.

## Slide 20: Thank you for your attention