## Slide 1
Alexander Ioffe
(chairman of the WSG-5)
Jülich Center for Neutron Science at Heinz Maier-Leibnitz Zentrum (Munich, Germany)
and
Frank Laboratory of Neutron Physics (JINR, Dubna)
WSG-5 on Condensed matter and neutron physics
for the Strategic Long-Term Plan of JINR
DNS-IV: a New Advanced Neutron Source at JINR
JINR Scientific Council Dubna 19.09.2019

## Slide 2
A. Ioffe (Germany) – Jülich Center for Neutron Science at Heinz Maier-Leibnitz Zentrum, München
Frank Laboratory of Neutron Physics JINR, Dubna (Chairman)
V.L. Aksenov (Russia) – National Research Center “Kurchatov Institute”, Moscow;
Frank Laboratory of Neutron Physics JINR, Dubna
J. Carpenter (USA) – Argonne National Laboratory, Chicago
A. Harrison (UK) – Diamond Light Source, Didcot, Member of JINR Scientific Council
N. Kucerka (Slovakia) – Frank Laboratory of Neutron Physics JINR, Dubna
T.V. Kulevoy (Russia) – National Research Center “Kurchatov Institute” – ITEP, Moscow
A.V. Lopatkin (Russia) – N.A. Dollezhal Research and Development Institute of Power Engineering (NIKIET), Moscow
F. Mezei (Sweden) – European Spallation Source, Lund
P. Mikula (Czech. Rep.) – Nuclear Physics Institute – Řež, Member of the JINR PAC on Condensed Matter Physics
D. Nagy (Hungary) – Wigner Research Centre for Physics, Budapest (Chairman of JINR PAC on Cond. Matter Physics)
V. Nesvizhevsky (France) – Institute Laue-Langevin, Grenoble, Member of JINR PAC on Nuclear Physics
L. Rosta (Hungary) – Budapest Neutron Center, Budapest
S.F. Sidorkin (Russia) – Institute for Nuclear Research of Russian Academy of Sciences, Troitsk Moscow Reg.
I.T. Tretyakov (Russia) – N.A. Dollezhal Research and Development Institute of Power Engineering (NIKIET), Moscow
D. Chudoba (Poland) – Frank Laboratory of Neutron Physics JINR, Dubna (scientific secretary)
Contribution on behalf of WSG-5 on condensed matter and neutron physics:

## Slide 3: Meetings and workshop
Regular semiannual meetings of the WSG-5:
June 15, 2018; January 23,2019; June 18, 2019
International Workshop (December 6-7, 2018):
46 participants from Sweden, France, Germany, Hungary, Slovakia, Poland and Russia
leading European and Russian neutron centers were represented.

## Slide 4: A New Advanced Neutron Source at JINR: Dubna Neutron Source (DNS-IV)
A long-term strategy aiming:
to construct a world leading neutron source DNS-IV at JINR
to open unprecedented possibilities for scientists from JINR member states and worldwide for research in condensed matter physics, fundamental physics, chemistry, material and life science.
Project is extended over two strategic planning periods, till 2036.
Estimated construction costs (incl. instrumentation) - about 500M€

## Slide 5
Condensed matter physics
(new materials, material design)
Information technologies (spintronics)
Fundamental physics
Life science: Biophysics, Pharmacology and Medicine – drug design and delivery
Engineering
Neutron Science – critical applications in:

## Slide 6: Neutrons are enormously important for Condensed Matter Physics
It explores the fundamental properties of matter and their origins resulting from the interactions of a large number of atoms and electrons
It explains the material world around us
It is the broadest field of physics, interconnecting the physics with chemistry, biology, geology, and astronomy, as well as nearly all fields of engineering
Notes: Condensed Matter Physics (CMP) explores the fundamental properties of matter and their origins resulting from the interactions of a large number of atoms and electrons. The intricate nature of these interactions results in properties and associated phenomena that often hint at a rich vein of underlying physics.
Condensed-matter and materials physics (CMMP) is the science of the material world around us. From the dawn of civilization, curiosity about the natural world has led to questions about the character of everyday substances such as water, snow, ice, and rocks, and how these respond to light, heat, and mechanical forces.
Materials and their behaviors are also key elements in other branches of science; as a result, CMMP is the broadest field of physics. Advances in CMMP have an impact that is immensely amplified by the intrinsic interconnectedness of CMMP with other fields of physics, chemistry, biology, geology, and astronomy, as well as nearly all fields of engineering.

## Slide 7: Neutrons vs. X-rays
Neutron scattering - no systematic A(Z) dependence => light elements are not masked by heavy ones
X-ray and neutron scattering power
X-rays: scattering  Z
Neutrons: irregular scattering
H+ is not visible for X-rays at the background of heavier atoms, but very well visible for neutrons!
Neutron energies: kTroom≈ 0.01eV (cf. 10-100 keV for X-rays)
=> non-disturbing and non-destructive probe;
=> much more sensitive to weak and slow atomic motions.
Neutrons: isotopic contrast! H/D difference – invaluable for biology
Neutron scattering clearly distinguish between neighboring atoms (for biology, particularly N, C and O)
Refining structure of proteins => drug design

## Slide 8: Neutrons vs. X-rays
H/D difference – isotopic contrast
H-protein contrast match
D2O
H2O
43% D2O
100% D2O
13% D2O
Scattering length density
0 --> 100% D2O
Contrast variation
Phospolipid contrast match
neutron anomalous magnetic moment => microspoic magnetic probe (polarized neutron scattering , polarimetry)
Zero charge => deep penetration (cm) without losses (cf. μm for X-rays)

## Slide 9: Fundamental physics at DNS-IV
traditional research with UCN (neutron lifetime measurement, neutron EDM search, precise measuring quantum states in gravitational field as tool for search new types of interaction, etc.);
new techniques for condense/soft matter and surface physics (high-resolution neutron microscopy, reflectometry);
Ultra cold neutrons (UCN) - wavelengths > 600Å
fundamental physics (search for neutron-antineutron oscillations; neutron lifetime measurements, search for extra-short-range interactions at neutron scattering, experiments with neutrons in a whispering gallery);
developing new techniques for condense/soft matter physics (high-resolution neutron spin-echo technique, reflectometry, high-resolution inelastic scattering, small angle scattering)
Very cold neutrons (VCN) - wavelengths 20Å to 100Å:

## Slide 10: European neutron landscape
PIK
FRM2
ЕSS
DUBNA
2036
2016
ILL
ISIS
FRM2
DUBNA
Inevitable shortage of neutron access
Clear need in a new neutron source

## Slide 11: World neutron landscape
PIK
FRM2
ЕSS
DUBNA
2036
2019
ILL
ISIS
FRM2
DUBNA
DNS-IV

## Slide 12: New Dubna neutron source
DNS-IV - not just another neutron source,
but one of the best in the world!
Pulsed neutron source: peak neutron flux instead of mean neutron flux.
IBR-2M
λ=1.5Å
IBR-2M
ESS
Mean flux of ILL
significant gain in the instrument performance
All neutron sources built during last two decades are pulsed sources (ISIS-2 (UK), J-PARC (Japan), SNS (USA).
European Spallation Source (ESS) – the most advanced neutron source (to be operational in 2024)
t
Reactor
source
Flux
Φmean
Φpeak
Pulsed source
T
τ
Instruments at ESS will outperform
similar instruments at ILL by 20-100 times!
New Dubna source will be benchmarked against the ESS.
Neutron pulses at different facilities

## Slide 13: New Dubna Neutron Source: DNS-IV
Long pulse neutron source, however shorter pulse than at ESS (0.3ms vs. 3ms)
10 times higher magnitude
DNS-IV: Φpeak~1016
IBR-2M
x10
λ=1.5Å
Mean flux of ILL
ESS long pulse is good for low resolution experiments
High resolution requires pulse shaping => intensity losses
New Dubna source will provide shorter neutron pulses, however containing the same number of neutrons as at ESS.
=> it will be as good as ESS for low resolution experiments and better for high resolution experiments.
Pulse shaping
DNS-IV - not just another neutron source, but one of the best in the world!

## Slide 14
Core +reflector
1. Pulsed reactor IBR-3
Reactivity modulator
Proton beam
Reactivity modulator
2. Accelerator-driven neutron source: spallation + multiplier
Core +reflector
E. Shabalin et al.
A. Vinogradov et al.
DNS-IV: two alternative concepts

## Slide 15
1. Pulsed reactor IBR-3
E. Shabalin et al.
DNS-IV: two alternative concepts
Reactivity modulator TiH2
1- Np-237 reactor core, 2 - empty sector of reactivity modulator, 3 - reactivity modulator coated with TiH2 , 4 - moderator, 5 – Be reflector.
From IBR-2 to IBR-3
DNS-IV
> 2036
thermal power of 10-12 MW
modified moderator placement geometry
=> neutron flux density 1014 n/cm2/s
Spherical core
to reduce the amount of Np-237.

## Slide 16
2. Accelerator-driven neutron source: spallation + multiplier
A. Vinogradov et al.
DNS-IV: two alternative concepts
Proton beam
Core + reflector
W target
PuO2
the same neutron flux as at ESS can be achieved by a 1.2GeV proton accelerator with the (20-50) times less beam power (0.1 MW vs. 5MW@ESS).
technical problems to be solved - the influence of instability of the accelerator’s operation on the stability of the operation of the booster.
PuO2 core operating in the deep under-critical mode
neutron multiplication factor of about 20-50

## Slide 17
Both options are under the feasibility study in N.A. Dollezhal Research and Development Institute of Power Engineering (NIKIET), Moscow
A positive feedback was already obtained for the IBR-3 project
Roadmap for design and construction of DNS-IV:
©NIKIET

## Slide 18
Both options are under the feasibility study in N.A. Dollezhal Research and Development Institute of Power Engineering (NIKIET), Moscow
A positive feedback was already obtained for the IBR-3 project
Roadmap for design and construction of DNS-IV:
©NIKIET

## Slide 19
Neutron source will be built in combination with proper moderators, neutron delivery system and instruments.
Highly efficient neutron source: maximal use of the emitted neutrons and neutrons delivered to instruments
Sample
Neutron Source
Delivery system
(neutron guide)
φemitted
φdelivered
Moderator
(spectra transformer)
Expected gain vs. IBR-2:
Flux | 10
Moderators | 2-3
Delivery system | 5-7
Instruments | 3-5
Total | 300-1000

## Slide 20: Plans for 2023-2030
1. Development of the final concept of modern thermal and cold moderators
Grooved moderators (high intensity)
32 beamports separated by 10°
CM-3
CM-4
CM-1
CM-2
80 K
(6 instr.)
30 K
(2 instr.)
300 / 80 K
(2 instr.)
30 K
(4 instr.)
30 K
(6 instr.)
30 K
(4 instr.)
Core
Low-dimensional moderators (high brilliance)
Converters for very cold neutrons (VCN/UCN factory)
time focusing of UCN at pulsed neutron beam.
construction of the VCN source prototype with directed extraction of neutron beam.
optimization of various moderators and UCN extraction systems for DNS-IV

## Slide 21: 2. Design of modern neutron instruments
Monte-Carlo simulations and optimization of neutron delivery system – maximal use of the emitted neutrons.
Monte-Carlo simulations and optimization of neutron scattering instruments – maximal use of the delivered neutrons.
Development of dedicated Monte-Carlo simulation procedures
4. IBR-2 Instrumentation Development
Construction, installation and commissioning of two inelastic neutron scattering spectrometers in inverted and direct geometry at the beamline #2;
Upgrade of the all IBR-2 instruments;
Design of the instruments for DNS-IV, testing the key technologies prototypes at the IBR-2;
Plans for 2023-2030
3. Design of the high-efficient neutron delivery system
Ballistic, elliptic and parabolic neutron guides

## Slide 22: Conclusions
Systematic shortage of the neutron beamtime in Europe and worldwide raises demand in construction the new neutron sources;
We propose the new advanced neutron source at JINR (DNS-IV) (the combination with modern moderators, neutron guides and instruments), which promises to be one of the best in the world;
DNS-IV will open unprecedented possibilities for scientists from JINR member states and worldwide for research in condensed matter physics, fundamental physics, chemistry, material and life science;
FLNP possesses the high-level competence in construction and operation of pulsed neutron sources, cold and ultra-cold neutron sources and neutron instrumentation;
FLNP is also staffed by a large number of motivated young scientists and engineers eager to work on this new exciting project;
The planned start of the DNS-IV operation is 2036-2037;

## Slide 23
Thank you for your attention!